Arria® V GX, GT, SX, and ST Device Schematic Review Worksheet

This document is intended to help you review your schematic and compare the pin usage against the Arria V Device Family Pin Connection Guidelines (PDF) version 1.9 and other referenced literature for this device family.  The technical content is divided into focus areas such as FPGA power supplies, transceiver power supplies and pin usage, configuration, and FPGA I/O, and external memory interfaces.

Within each focus area, there is a table that contains the voltage or pin name for all of the dedicated and dual purpose pins for the device family.  In some cases, the device density and package combination may not include some of the pins shown in this worksheet, you should cross reference with the pin-out file for your specific device.  Links to the device pin-out files are provided at the top of each section.

Before you begin using this worksheet to review your schematic and commit to board layout, Altera highly recommends:

1) Review the latest version of the Errata Sheet and Guidelines for Arria V ES Devices (PDF), Errata Sheet for Arria V Devices (PDF), and the Knowledge Database for Arria V Device Known Issues and Arria V Device Handbook Known Issues.

2)  Compile your design in the Quartus® II software to completion.

For example, there are many I/O related placement restrictions and VCCIO requirements for the I/O standards used in the device.  If you do not have a complete project, then at a minimum a top level project should be used with all I/O pins defined, placed, and apply all of the configurable options that you plan to use.  All I/O related megafunctions should also be included in the minimal project, including, but not limited to, external memory interfaces, transceiver IP, PLLs, altlvds, and altddio.  The I/O Analysis tool in the Pin Planner can then be used on the minimal project to validate the pinout in the Quartus II software to assure there are no conflicts with the device rules and guidelines.

When using the I/O Analysis tool you must ensure there are no errors with your pinout.  Additionally, you should check all warning and critical warning messages to evaluate their impact on your design.  You can right click your mouse over any warning or critical warning message and select “Help”.  This will bring open a new Help window with further information on the cause of the warning, and the action that is required.

For example, the following warning is generated when a PLL is driven by a global network where the source is a valid dedicated clock input pin, but the pin is not one dedicated to the particular PLL:

Warning: PLL "<PLL Instance Name>" input clock inclk[0] is not fully compensated and may have reduced jitter performance because it is fed by a non-dedicated input

Info: Input port INCLK[0] of node "<PLL Instance Name>" is driven by clock~clkctrl which is OUTCLK output port of Clock Control Block type node clock~clkctrl

The help file provides the following:

| CAUSE: | The specified PLL's input clock is not driven by a dedicated input pin. As a result, the input clock delay will not be fully compensated by the PLL. Additionally, jitter performance depends on the switching rate of other design elements. This can also occur if a global signal assignment is applied to the clock input pin, which forces the clock to use the non-dedicated global clock network. |
| --- | --- |
| ACTION: | If you want compensation of the specified input clock or better jitter performance, connect the input clock only to an input pin, or assign the input pin only to a dedicated input clock location for the PLL. If you do not want compensation of the specified input clock, then set the PLL to No Compensation mode. |

When assigning the input pin to the proper dedicated clock pin location, refer to Clock Networks and PLLs in Arria V Devices (PDF) for the proper port mapping of dedicated clock input pins to PLLs.

There are many reports available for use after a successful compilation or I/O analysis.  For example, you can use the “All Package Pins” and “I/O Bank Usage” reports within the Compilation – Fitter – Resource Section to see all of the I/O standards and I/O configurable options that are assigned to all of the pins in your design, as well as view the required VCCIO for each I/O bank.  These reports must match your schematic pin connections.

The review table has the following heading:

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |

The first column (Plane/Signal) lists the FPGA voltage or signal pin name.  You should only edit this column to remove dedicated or dual purpose pin names that are not available for your device density and package option.

The second column (Schematic Name) is for you to enter your schematic name(s) for the signal(s) or plane connected to the FPGA pin(s).

The third column (Connection Guidelines) should be considered “read only” as this contains Altera’s recommended connection guidelines for the voltage plane or signal.

The fourth column (Comments/Issues) is an area provided as a “notepad” for you to comment on any deviations from the connection guidelines, and to verify guidelines are met.  In many cases there are notes that provide further information and detail that compliment the connection guidelines.

Here is an example of how the worksheet can be used:

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| <Plane / Signal name provided by Altera> VCC | <user entered text> +1.1V | <Device Specific Guidelines provided by Altera> | <user entered text> Connected to +1.1V plane, no isolation is necessary. Missing low and medium range decoupling, check PDN. |

Legal Note:

PLEASE REVIEW THE FOLLOWING TERMS AND CONDITIONS CAREFULLY BEFORE USING THIS SCHEMATIC REVIEW WORKSHEET (“WORKSHEET”) PROVIDED TO YOU. BY USING THIS WORKSHEET, YOU INDICATE YOUR ACCEPTANCE OF SUCH TERMS AND CONDITIONS, WHICH CONSTITUTE THE LICENSE AGREEMENT ("AGREEMENT") BETWEEN YOU AND ALTERA CORPORATION OR ITS APPLICABLE SUBSIDIARIES ("ALTERA").

1. Subject to the terms and conditions of this Agreement, Altera grants to you, for no additional fee, a non-exclusive and non-transferable right to use this Worksheet for the sole purpose of verifying the validity of the pin connections of an Altera programmable logic device-based design. You may not use this Worksheet for any other purpose.  There are no implied licenses granted under this Agreement, and all rights, except for those granted under this Agreement, remain with Altera.

2. Altera does not guarantee or imply the reliability, or serviceability, of this Worksheet or other items provided as part of this Worksheet. This Worksheet is provided 'AS IS'. ALTERA DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING THE IMPLIED WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, AND NON-INFRINGEMENT.  ALTERA HAS NO OBLIGATION TO PROVIDE YOU WITH ANY SUPPORT OR MAINTENANCE.

3. In no event shall the aggregate liability of Altera relating to this Agreement or the subject matter hereof under any legal theory (whether in tort, contract, or otherwise), exceed One Hundred US Dollars (US$100.00). In no event shall Altera be liable for any lost revenue, lost profits, or other consequential, indirect, or special damages caused by your use of this Worksheet even if advised of the possibility of such damages.

4. This Agreement may be terminated by either party for any reason at any time upon 30-days’ prior written notice.  This Agreement shall be governed by the laws of the State of California, without regard to conflict of law or choice of law principles. You agree to submit to the exclusive jurisdiction of the courts in the County of Santa Clara, State of California for the resolution of any dispute or claim arising out of or relating to this Agreement. The parties hereby agree that the party who is not the substantially prevailing party with respect to a dispute, claim, or controversy relating to this Agreement shall pay the costs actually incurred by the substantially prevailing party in relation to such dispute, claim, or controversy, including attorneys' fees.  Failure to enforce any term or condition of this Agreement shall not be deemed a waiver of the right to later enforce such term or condition or any other term or condition of the Agreement.

BY USING THIS WORKSHEET, YOU ACKNOWLEDGE THAT YOU HAVE READ THIS AGREEMENT, UNDERSTAND IT, AND AGREE TO BE BOUND BY ITS TERMS AND CONDITIONS. YOU AND ALTERA FURTHER AGREE THAT IT IS THE COMPLETE AND EXCLUSIVE STATEMENT OF THE AGREEMENT BETWEEN YOU AND ALTERA, WHICH SUPERSEDES ANY PROPOSAL OR PRIOR AGREEMENT, ORAL OR WRITTEN, AND ANY OTHER COMMUNICATIONS BETWEEN YOU AND ALTERA RELATING TO THE SUBJECT MATTER OF THIS AGREEMENT.

Index

Section I: 	Power

Section II: 	Configuration

Section III: 	Transceiver

Section IV: 	I/O

a:	Clock Pins

b:	Dedicated and Dual Purpose Pins

c: 	Dual Purpose Differential I/O pins

d:          HPS I/O

Section V: 	External Memory Interface Pins

a:	DDR3/DDR3L Interface Pins

b: 	DDR3/DDR3L Termination Guidelines

c: 	DDR2 Interface Pins

d: 	DDR2 Termination Guidelines

e: 	LPDDR2 Interface Pins

f: 	LPDDR2 Termination Guidelines

g:	QDRII/+ Interface pins

h:	QDRII/+ Termination Guidelines

Section VI:	Document Revision History

Section I: Power

Documentation: Arria V Devices

Arria V Device Pin-Out Files

Arria V Device Family Pin Connection Guidelines (PDF)

Arria V Early Power Estimator

Arria V Early Power Estimator User Guide (PDF)

Power Delivery Network (PDN) Tool For Arria V Devices

Device-Specific Power Delivery Network (PDN) Tool User Guide (PDF)

PowerPlay Power Analyzer Support Resources

Altera Board Design Resource Center (General board design guidelines, PDN design, isolation, tools, and more)

AN 583: Designing Power Isolation Filters with Ferrite Beads for Altera FPGAs (PDF)

AN 597: Getting Started Flow for Board Designs (PDF)

Errata Sheet and Guidelines for Arria V ES Devices (PDF)

Errata Sheet for Arria V Devices (PDF)

Known Arria V Issues

Index

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCC |  | For Arria V GX -C4, -C5, -I5, and -C6 and Arria V GT -I5 devices: Connect all VCC pins to a 1.1V low noise switching regulator. For Arria V GX -I3 and GT -I3 devices: Connect all VCC pins to a 1.15V low noise switching regulator. VCC may be sourced from the same regulator as VCCP with a proper isolation filter. Use the Arria V Early Power Estimator to determine the current requirements for VCC and other supplies. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-3) (1-4) (1-5). |
| VCCP |  | For Arria V GX -C4, -C5, -I5, and -C6 and Arria V GT -I5 devices: Connect all VCCP pins to a 1.1V low noise switching regulator. For Arria V GX -I3 and GT –I3 devices: Connect all VCCP pins to a 1.15V low noise switching regulator. VCCP may be sourced from the same regulator as VCC with a proper isolation filter. Separate VCC and VCCP planes into two different power layers on the PCB. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-3) (1-4) (1-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCC_HPS (Arria V SoC device variants only) |  | Power supply for the HPS core. For Arria V SX and ST devices except Arria V SX and ST –I3 devices, connect all VCC_HPS pins to a 1.1V low noise switching regulator. for Arria V SX and ST –I3 devices, connect all VCC_HPS pins to a 1.15V low noise switching regulator. If powering down of the FPGA fabric is not required, VCC_HPS pins may be sourced from the same regulator as VCC with a proper isolation filter. Use the Arria V Early Power Estimator to determine the current requirements for VCC_HPS and other supplies. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-3) (1-4) (1-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCIO[3,4,7,8] [A,B,C,D] (not all pins are available in each device / package combination) |  | Connect these pin to 1.2V, 1.25V, 1.35V, 1.5V, 1.8V, 2.5V, 3.0V, or 3.3V supplies, depending on the I/O standard connected to the specified bank. When these pins require the same voltage level as VCCPD and / or VCCPGM, they may be tied to the same regulator as VCCPD and / or VCCPGM. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCIO[6,7][A,B]_HPS, VCCIO7[C,D,E]_HPS (Arria V SoC device variants only) (not all pins are available in each device / package combination) |  | Connect these pin to 1.2V, 1.5V, 1.8V, 2.5V, 3.0V, or 3.3V supplies, depending on the I/O standard connected to the specified bank. When these pins require the same voltage level as VCCPD_HPS and / or VCCRSTCLK_HPS, they may be tied to the same regulator. If powering down of the FPGA fabric is not required and if these pins have the same voltage requirement as VCCIO, VCCIO_HPS pins may be sourced from the same regulator as VCCIO. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCPD3 VCCPD4A VCCPD4[BCD] VCCPD7A VCCPD7[BCD] VCCPD8 (not all pins are available in each device / package combination) |  | The VCCPD pins require 2.5V, 3.0V, or 3.3V. VCCPD voltage connection depends on the VCCIO voltage of the bank. VCCPD is 3.3V for 3.3V VCCIO. VCCPD is 3.0V for 3.0V VCCIO. VCCPD is 2.5V for 2.5V/1.8V/1.5V/1.35V/1.25V/1.2V VCCIO. When these pins require the same voltage level as VCCIO and / or VCCPGM, they may be tied to the same regulator as VCCIO and / or VCCPGM. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCPD6A6B_HPS VCCPD7[A,B,C,D,E]_HPS (Arria V SoC device variants only) (not all pins are available in each device / package combination) |  | The VCCPD pins require 2.5V, 3.0V, or 3.3V. When these pins have the same voltage requirements as VCCRSTCLK_HPS and VCCIO_HPS, they may be tied to the same regulator. If powering down of the FPGA fabric is not required and if these pins have the same voltage requirement as VCCPD, VCCIO, and VCCPGM, they may be tied to the same regulator. VCCPD voltage connection depends on the VCCIO voltage of the bank. VCCPD_HPS is 3.3V for 3.3V VCCIO_HPS. VCCPD_HPS is 3.0V for 3.0V VCCIO_HPS. VCCPD_HPS is 2.5V for 2.5V/1.8V/1.5V/1.2V VCCIO_HPS. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCPGM |  | Connect these pins to either 1.8V, 2.5V, 3.0V, or 3.3V. When these pins require the same voltage level as VCCIO and / or VCCPD, they may be tied to the same regulator as VCCIO and / or VCCPD. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VREF[3,4,7,8] [A,B,C,D]N0 (not all pins are available in each device / package combination) |  | These are dual purpose pins. When used for their dedicated function, they are the input reference voltage for each I/O bank. If a bank uses a voltage referenced I/O standard, then these pins are used as the voltage-reference pins for the I/O bank. When not used as a voltage reference input, these pins can be used as I/O pins. When used as I/O pins, they have higher capacitance than regular I/O pins which will slow the edge rates and affect I/O timing. Avoid placing fast edge rate signals such as clocks on these pins, and avoid using these pins in buses since the I/O timing will not be consistent with the rest of the bus. If VREF pins are not used for their dedicated function or as regular I/O pins, you should connect them to either the VCCIO in the bank where the pin resides or GND. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Note (1-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VREFB6[A,B]N0_HPS, VREFB7A7B7C7D7EN0_HPS (Arria V SoC device variants only) (not all pins are available in each device / package combination) |  | Input reference voltage for each I/O bank. If a bank uses a voltage referenced I/O standard for input operation, then these pins are used as the voltage-reference pins for the bank. If the VREF pins are not used, you should connect them to either the VCCIO in the bank in which the pin resides or GND. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Note (1-1). |
| VCCRSTCLK_HPS (Arria V SoC device variants only) |  | VCCRSTCLK_HPS supplies power to HPS clock and reset pins. Connect these pins to either a 1.8V, 2.5V, 3.0V, or 3.3V power supply. When these pins have the same voltage requirements as VCCIO_HPS and VCCPD_HPS, they may be tied to the same regulator. If powering down of the FPGA fabric is not required and if these pins have the same voltage requirement as VCCIO, VCCPGM, and VCCPD, they may be tied to the same regulator. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-3) (1-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCD_FPLL |  | Connect all VCCD_FPLL pins to a 1.5V linear or low noise switching power supply. These pins may be tied to the same regulator as VCCBAT and VCCH_GXB. These supplies may share power planes across multiple Arria V devices. If any PLLs are used in the device, you must ensure the proper RREF_BR and RREF_TL pins are connected to their own individual 2.0-kΩ +/- 1% resistor to GND (see transceiver section of this review for details). Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-3) (1-5). |
| VCCA_FPLL |  | Connect these pins to a 2.5V low noise switching power supply through a proper isolation filter. This power rail may be shared with VCCAUX and VCCA_GXB. With a proper isolation filter these pins may be sourced from the same regulator as VCCIO, VCCPD, and VCCPGM when each of these supplies require 2.5V. This supply may share power planes across multiple Arria V devices. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-3) (1-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCPLL_HPS (Arria V SoC device variants only) |  | VCCPLL_HPS supplies power to the HPS core PLLs. Connect these pins to a 2.5V low noise switching power supply through a proper isolation filter. This power rail may be shared with the VCC_AUX_SHARED pin. If powering down of the FPGA fabric is not required and with a proper isolation filter, these pins may be sourced from the same regulator as VCCIO, VCCPD, VCCPGM, VCCIO_HPS, VCCPD_HPS, and VCCRSTCLK_HPS when each of these power supplies require 2.5V. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-3) (1-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCC_AUX |  | Connect all VCC_AUX pins to a 2.5V low noise switching power supply through a proper isolation filter. For Arria V GX and GT devices, this power rail may be shared with VCCA_FPLL and VCCA_GXB. With a proper isolation filter these pins may be sourced from the same regulator as VCCIO, VCCPD, and VCCPGM when each of these power supplies require 2.5V. For Arria V SX and ST device, VCC_AUX must always be powered up for the PLL operation and if powering down the FPGA fabric is not required, this power rail may be shared with VCC_AUX_SHARED, VCCA_GXB, and VCCA_FPLL. With a proper isolation filter these pins may be sourced from the same regulator as VCCIO, VCCIO_HPS, VCCPD, VCCPD_HPS, VCCPGM, and VCCRSTCLK_HPS when each of these power supplies require 2.5V. These supplies may share power planes across multiple Arria V devices. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-3) (1-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCC_AUX_SHARED (Arria V SoC device variants only) |  | VCC_AUX_SHARED must always be powered up at 2.5V for the HPS operation. This pin may be tied together to the same regulator as VCCPLL_HPS. If powering down of the FPGA fabric is not required, this power rail may be shared with VCC_AUX, VCCA_GXB, and VCCA_FPLL pins. Connect this pin to VCC_AUX using a proper isolation filter. With a proper isolation filter, these pins may be sourced from the same regulator as VCCIO, VCCIO_HPS, VCCPD, VCCPD_HPS, VCCPGM and VCCRSTCLK_HPS when each of these power supplies requires 2.5V. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-3) (1-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCBAT |  | Connect this pin to a non-volatile battery power source in the range of 1.2V – 3.0V when using the design security volatile key. In this case, do not connect this pin to a volatile power source on the board. 3.0V is the typical power selected for this supply. When not using the volatile key, tie this to a 1.5V, 2.5V, or 3.0V supply. Arria V devices will not exit POR if VCCBAT stays at logic low. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. |
| GND |  | All GND pins must be connected to the board ground plane. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |

Index  Top of Section

Notes:

1-1. This worksheet does not calculate required decoupling, it is expected the designer will select decoupling based on analysis of power required and impedance of power path required based on static and switching current values.  Refer to Altera’s Power Delivery Network (PDN) Tool for Arria V Devices for further information.

Capacitance values for the power supply should be selected after consideration of the amount of power they need to supply over the frequency of operation of the particular circuit being decoupled. A target impedance for the power plane should be calculated based on current draw and voltage drop requirements of the device/supply. The power plane should then be decoupled using the appropriate number of capacitors. On-board capacitors do not decouple higher than 100 MHz due to “Equivalent Series Inductance” of the mounting of the packages. Proper board design techniques such as interplane capacitance with low inductance should be considered for higher frequency decoupling.

1-2. This worksheet does not include power estimation for the different power supplies provided. Ensure each power supply is adequate for the device current requirements.  Refer to Altera’s Early Power Estimation Tools and PowerPlay Power Analyzer Support Resources for further guidance.

Use Altera’s Early Power Estimation Tools to ensure the junction temperature of the device is within operating specifications based on your design activity.

1-3. Low Noise Switching Regulator is defined as a switching regulator circuit encapsulated in a thin surface mount package containing the switch controller, power FETs, inductor, and other support components.  The switching frequency is usually between 800kHz and 1MHz and has a fast transient response.  The switching frequency range is not an Altera requirement. However, Altera does require the Line Regulation and Load Regulation meet the following requirements:

- Line Regulation < 0.4%.

- Load Regulation < 1.2%

1-4. Power pins should not share breakout vias from the BGA.  Each ball on the BGA needs to have its own dedicated breakout via.  VCC must not share breakout vias.

1-5. These supplies may share power planes across multiple Arria V devices.

Index  Top of Section

Reviewed against Errata Sheet for Arria V Devices (PDF) version:

Additional Comments:

Index  Top of Section

Section II: Configuration

Arria V Recommended Reference Literature/Tool List

Arria V Pin-Out Files

Arria V Device Family Pin Connection Guidelines (PDF)

Configuration, Design Security, and Remote System Upgrades in Arria V Devices (PDF)

JTAG Boundary-Scan Testing in Arria V Devices (PDF)

USB-Blaster Download Cable User Guide (PDF)

ByteBlaster II Download Cable User Guide (PDF)

EthernetBlaster II Communications Cable User Guide (PDF)

AN 597: Getting Started Flow for Board Designs (PDF)

Errata Sheet and Guidelines for Arria V ES Devices (PDF)

Errata Sheet for Arria V Devices (PDF)

Index

| Configuration Scheme | Configuration Voltage |  |
| --- | --- | --- |

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| MSEL[0:4] |  | These pins are internally connected through a 25-kΩ resistor to GND. Do not leave these pins floating. When these pins are unused connect them to GND. Depending on the configuration scheme used these pins should be tied to VCCPGM or GND. Refer to Configuration, Design Security, and Remote System Upgrades in Arria V Devices (PDF) for the configuration scheme options. If only JTAG configuration is used, connect these pins to ground. | Verify Guidelines have been met or list required actions for compliance. |
| nCE |  | Dedicated active-low chip enable. When nCE is low, the device is enabled. When nCE is high, the device is disabled. In multi-device configuration, nCE of the first device is tied low while its nCEO pin drives the nCE of the next device in the chain. In single device configuration and JTAG programming, nCE should be connected to GND or through a 10-kΩ pull-down to GND if using an Active Serial header. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| nCONFIG |  | Dedicated configuration control input. Pulling this pin low during user-mode will cause the FPGA to lose its configuration data, enter a reset state, and tri-state all I/O pins. Returning this pin to a logic high level will initiate reconfiguration. nCONFIG should be connected directly to the configuration controller when the FPGA uses a passive configuration scheme, or through a 10-kΩ resistor tied to VCCPGM when using an active serial configuration scheme. If this pin is not used, it requires a connection directly or through a 10-kΩ resistor to VCCPGM. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| CONF_DONE |  | This is a dedicated configuration done pin. As a status output, the CONF_DONE pin drives low before and during configuration. Once all configuration data is received without error and the initialization cycle starts, CONF_DONE is released. As a status input, CONF_DONE goes high after all data is received. Then the device initializes and enters user mode. It is not available as a user I/O pin. If internal pull-up resistors on the configuration controller are used, external 10-kΩ pull-up resistors should not be used on this pin. Otherwise, use an external 10-kΩ pull-up resistor to VCCPGM should be used. When using passive configuration schemes this pin should also be monitored by the configuration controller. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| nCEO |  | During multi-device configuration, this pin feeds the nCE pin of a subsequent device. Connect this pin to an external 10-kΩ pull-up resistor to VCCPGM. During single device configuration, this pin may be left floating. This pin is not available for regular I/O usage in multi-device configuration mode, see rd04132011_29. | Verify Guidelines have been met or list required actions for compliance. |
| nSTATUS |  | This is a dedicated configuration status pin. The FPGA drives nSTATUS low immediately after power-up and releases it after POR time. As a status output, the nSTATUS is pulled low if an error occurs during configuration. As a status input, the device enters an error state when nSTATUS is driven low by an external source during configuration or initialization. It is not available as a user I/O pin. When using Passive configuration schemes this pin should also be monitored by the configuration controller. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| TCK |  | Connect this pin to a 1-kΩ pull-down resistor to GND. This pin has an internal 25-kΩ pull-down. Treat this signal like a clock and follow typical clock routing guidelines. | Verify Guidelines have been met or list required actions for compliance. |
| TMS |  | Connect this pin to a 1-kΩ - 10-kΩ pull-up resistor to VCCPD. To disable the JTAG circuitry connect TMS to VCCPD via a 1-kΩ resistor. This pin has an internal 25-kΩ pull-up. | Verify Guidelines have been met or list required actions for compliance. |
| TDI |  | Connect this pin to a 1-kΩ - 10-kΩ pull-up resistor to VCCPD. To disable the JTAG circuitry connect TDI to VCCPD via a 1-kΩ resistor. This pin has an internal 25-kΩ pull-up. | Verify Guidelines have been met or list required actions for compliance. |
| TDO |  | The JTAG circuitry can be disabled by leaving TDO unconnected. In cases where TDO uses VCCPD = 2.5 V to drive a 3.3V JTAG interface, there may be leakage current in the TDI input buffer of the interfacing devices. An external pull-up resistor tied to 3.3 V on their TDI pin may be used to eliminate the leakage current if needed. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Optional Dual Purpose Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| DCLK |  | Dedicated configuration clock pin. In PS and FPP configuration, DCLK is used to clock configuration data from an external source into the FPGA. In AS mode, DCLK is an output from the FPGA that provides timing for the configuration interface. Do not leave this pin floating. Drive this pin either high or low. DCLK can be configured to be a user I/O pin after configuration when the configuration mode is an Active mode. | Verify Guidelines have been met or list required actions for compliance. |
| CRC_ERROR |  | This pin is optional and is used when the CRC error detection circuit is enabled. When using as optionally open-drain output dedicated CRC_ERROR pin, connect this pin to an external 10-kΩ pull-up resistor to VCCPGM. When not using as the dedicated CRC_ERROR pin, and when not using as a user I/O, connect this pin as defined in the Quartus II software. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| External Memory Interface Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| AS_DATA0 / ASDO / DATA[0] |  | Dedicated AS configuration pin. When using an EPCS device (x1 mode) this is the ASDO pin and used to send address and control signals between the FPGA and the EPCS/EPCQ. Used as DATA[0] for FPP and PS modes. When not programming the device in AS mode ASDO is not used. Also, when this pin is not used it is recommended to leave the pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| AS_DATA[1:3] / DATA[1:3] |  | Dedicated AS configuration data pins. Configuration data is transported on these pins when connected to the EPCQ devices. Used as DATA[1:3 for FPP mode. When this pin is not used it is recommended to leave the pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| nCSO / DATA[4] |  | Dedicated output control signal from the FPGA to the serial configuration device in AS mode that enables the configuration device. When not programming the device in AS mode nCSO is not used. Also, when this pin is not used as an output then it is recommended to leave the pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Partial Reconfiguration Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| PR_REQUEST |  | Partial Reconfiguration Request pin. Drive this pin high to start partial reconfiguration. Drive this pin low to end reconfiguration. This pin can only be used in Partial Reconfiguration using external host mode in FPP x16 configuration scheme. When the dedicated input PR_REQUEST is not used and this pin is not used as an I/O, then it is recommended to tie this pin to GND. | Verify Guidelines have been met or list required actions for compliance. |
| PR_READY |  | When using as optionally open-drain output dedicated PR_READY pin, connect this pin to an external 10-kΩ pull-up resistor to VCCPGM. When not using as the dedicated PR_READY optionally open-drain output, and when this pin is not used as an I/O pin, then connect this pin as defined in the Quartus II software. | Verify Guidelines have been met or list required actions for compliance. |
| PR_ERROR |  | When using as optionally open-drain output dedicated PR_ERROR pin, connect this pin to an external 10-kΩ pull-up resistor to VCCPGM. When not using as the dedicated PR_ERROR optionally open-drain output, and when this pin is not used as an I/O pin, then connect this pin as defined in the Quartus II software. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| PR_DONE |  | When using as optionally open-drain output dedicated PR_DONE pin, connect this pin to an external 10-kΩ pull-up resistor to VCCPGM. When not using as the dedicated PR_DONE optionally open-drain output, and when this pin is not used as an I/O pin, then connect this pin as defined in the Quartus II software. | Verify Guidelines have been met or list required actions for compliance. |
| CvP_CONFDONE |  | When using as optionally open-drain output dedicated CvP_CONFDONE pin, connect this pin to an external 10-kΩ pullup resistor to VCCPGM. When not using as the dedicated CvP_CONFDONE optionally open-drain output, and when this pin is not used as an I/O pin, then connect this pin as defined in the Quartus II software. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DEV_CLRn |  | This pin is optional and allows you to override all clears on all device registers. When the dedicated input DEV_CLRn is not used and this pin is not used as an I/O then it is recommended to tie this pin to ground. | Verify Guidelines have been met or list required actions for compliance. |
| DEV_OE |  | This pin is optional and allows you to override all tri-states on the device. When the dedicated input DEV_OE is not used and this pin is not used as an I/O then it is recommended to tie this pin to ground. | Verify Guidelines have been met or list required actions for compliance. |
| DATA[5:15] |  | Dual-purpose configuration input data pins and user I/O pins after configuration. For FPP x8 use DATA[5:7] For FPP x16 use DATA[5:15] When the dedicated inputs for DATA[5:15] are not used and these pins are not used as an I/O then it is recommended to leave these pins unconnected. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| INIT_DONE |  | This is a dual-purpose pin and can be used as an I/O pin when not enabled as INIT_DONE. When using as optionally open-drain output dedicated INIT_DONE pin, a transition from low to high at the pin indicates when the device has entered user mode. The INIT_DONE pin cannot be used as a user I/O pin after configuration. Connect this pin to an external 10-kΩ pull-up resistor to VCCPGM. When not using as the dedicated INIT_DONE pin, and when this pin is not used as an I/O pin, then connect this pin as defined in the Quartus II software. | Verify Guidelines have been met or list required actions for compliance. |
| CLKUSR |  | Optional user-supplied clock input which synchronizes the initialization of one or more devices. If not enabled as user-supplied configuration clock, it can be used as a user I/O pin. If the CLKUSR pin is not used as a configuration clock input and the pin is not used as an I/O then it is recommended to connect this pin to ground. Set this pin “as output driving ground” in the Quartus II software using the “Reserve Pins” assignment. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| JTAG Header |  | Power the EthernetBlaster II, ByteBlaster II or USB-Blaster cable’s VCC (pin 4 of the header) with VCCPD. For multi-device JTAG chains with different VCCIO voltages, voltage translators may be required to meet the I/O voltages for the devices in the chain and JTAG header. The EthernetBlaster II, ByteBlaster II and USB-Blaster cables do not support a target supply voltage of 1.2 V. For the target supply voltage value, refer to the EthernetBlaster II Communications Cable User Guide, ByteBlaster II Download Cable User Guide and the USB-Blaster Download Cable User Guide. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| HPS Configuration and JTAG Pins |  |  |
| --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| BOOTSEL[2:0] (Arria V SoC device variants only) |  | During a cold reset this signal is sampled as a boot select input. Connect a pull-up or pull-down resistor such as 4.7-kΩ - 10-kΩ to select the desired boot select values. This resistor will not interfere with the slow speed interface signals that could share this pin. Refer to table A-1 in Booting and Configuration (PDF) for BSEL values. Ensure the selected boot device is present on the schematic. | Verify Guidelines have been met or list required actions for compliance. |
| CLKSEL[1:0] (Arria V SoC device variants only) |  | During a cold reset this signal is sampled as a clock select input. Connect a pull-up or pull-down resistor such as 4.7-kΩ - 10-kΩ to select the desired clock select values. This resistor will not interfere with the slow speed interface signals that could share this pin. Refer to the appropriate CSEL table in Booting and Configuration (PDF) for Clock Select values. NAND: Table A-4 SD/MMC: Table A-8 QSPI: Table A-10 | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| HPS_TDI (Arria V SoC device variants only) |  | JTAG test Data input pin for instructions as well as test and programming data. Data is shifted in on the rising edge of the TCK pin. This pin has an internal 25-kΩ pull-up resistor that is always active. Connect this pin through a 1-kΩ - 10-kΩ pull-up resistor to VCCPD_HPS in the dedicated I/O bank which the JTAG pin resides. To disable the JTAG circuitry, connect the TDI pin to VCCPD_HPS using a 1-kΩ resistor. | Verify Guidelines have been met or list required actions for compliance. |
| HPS_TMS (Arria V SoC device variants only) |  | This pin has an internal 25-kΩ pull-up resistor that is always active. Connect this pin through a 1-kΩ - 10-kΩ - pull-up resistor to the VCCPD_HPS in the dedicated I/O bank which the JTAG pin resides. To disable the JTAG circuitry, connect the TMS pin to VCCPD_HPS using a 1-kΩ resistor. | Verify Guidelines have been met or list required actions for compliance. |
| HPS_TRST (Arria V SoC device variants only) |  | Active-low input to asynchronously reset the boundary-scan circuit. This pin has an internal 25-kΩ pull-up that is always active. Connect this pin through a 1-kΩ - 10-kΩ pull-up resistor to the VCCPD_HPS in the dedicated I/O bank which the JTAG pin resides. | Verify Guidelines have been met or list required actions for compliance. |

Index Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| HPS_TCK (Arria V SoC device variants only) |  | JTAG test clock input pin that clock input to the boundary-scan testing (BST) circuitry. This pin has an internal 25-kΩ pull-down that is always active. Connect this pin through a 1-kΩ - 10-kΩ pull-down resistor to GND. Treat this signal like a clock and follow typical clock routing guidelines. | Verify Guidelines have been met or list required actions for compliance. |
| HPS_TDO (Arria V SoC device variants only) |  | JTAG test Data output pin for instructions as well as test and programming Data. To disable the JTAG circuitry, leave the HPS_TDO pin unconnected. In cases where the HPS_TDO pin uses VCCPD_HPS = 2.5 V to drive a 3.3 V JTAG interface, there may be leakage current in the HPS_TDI input buffer of the interfacing devices. An external pull-up resistor tied to 3.3 V on the HPS_TDI pin may be used to eliminate the leakage current if needed. | Verify Guidelines have been met or list required actions for compliance. |

Index Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| HPS_nRST (Arria V SoC device variants only) |  | Warm reset to the HPS block. This pin has an internal 25-kΩ pull-up resistor that is always active. Connect this pin through a 1-kΩ - 10-kΩ pull-up resistor to VCCRSTCLK_HPS. | Verify Guidelines have been met or list required actions for compliance. |
| HPS_nPOR (Arria V SoC device variants only) |  | Cold reset to the HPS block. This pin has an internal 25-kΩ pull-up resistor that is always active. Connect this pin through a 1-kΩ - 10-kΩ pull-up resistor to VCCRSTCLK_HPS. | Verify Guidelines have been met or list required actions for compliance. |
| HPS_PORSEL (Arria V SoC device variants only) |  | Dedicated input that selects between a standard POR or a fast POR delay for HPS block. A logic low selects a standard POR delay setting and a logic high selects a fast POR delay setting. This pin has an internal 25-kΩ pull-down resistor that is always active. Connect this pin directly to VCCRSTCLK_HPS or GND. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| JTAG Header (HPS) (Arria V SoC device variants only) |  | Power the ByteBlaster II or USB-Blaster cable’s VCC (pin 4 of the header) with VCCIO7A voltage. For multi-device JTAG chains with different VCCIO voltages, voltage translators may be required to meet the I/O voltages for the devices in the chain and JTAG header. The ByteBlaster II and USB-Blaster cables do not support a target supply voltage of 1.2 V. For the target supply voltage value, refer to the ByteBlaster II Download Cable User Guide and the USB-Blaster Download Cable User Guide. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

Reviewed against Errata Sheet for Arria V Devices (PDF) version:

Additional Comments:

Index  Top of Section

Section III: Transceiver

Documentation: Arria V Devices

Arria V Device Pin-Out Files

Arria V Device Family Pin Connection Guidelines (PDF)

Arria V Early Power Estimator

Arria V Early Power Estimator User Guide (PDF)

Power Delivery Network (PDN) Tool For Arria V Devices

Device-Specific Power Delivery Network (PDN) Tool User Guide (PDF)

Altera Board Design Resource Center (General board design guidelines, PDN design, isolation, tools, and more)

AN 597: Getting Started Flow for Board Designs (PDF)

Altera Board Design Resource Center (General board design guidelines, PDN design, isolation, tools, and more)

AN 583: Designing Power Isolation Filters with Ferrite Beads for Altera FPGAs (PDF)

Arria V Hard IP for PCI Express User Guide (PDF)

Errata Sheet and Guidelines for Arria V ES Devices (PDF)

Errata Sheet for Arria V Devices (PDF)

Known Arria V Issues

Index

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCA_GXB[L,R][0:3] (not all pins are available in each device / package combination) |  | Analog power, transceiver high voltage, specific to the left (L) side or right (R) side of the device. Connect VCCA_GXB to a 2.5V low noise switching regulator. This power rail may be shared with VCCA_FPLL and VCC_AUX. With a proper isolation filter these pins may be sourced from the same regulator as VCCIO, VCCPD and VCCPGM, when each of these power supplies require 2.5V. Decoupling depends on the design decoupling requirements of the specific board design. | Verify Guidelines have been met or list required actions for compliance. See Notes (3-1) (3-2) (3-3) (3-4) (3-5) (3-7). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCH_GXB[L,R][0:3] (not all pins are available in each device / package combination) |  | Analog power, transmitter output buffer specific to the left (L) side or right (R) side of the device. Connect VCCH_GXB to a 1.5V linear or low noise switching regulator. These pins may be sourced from the same regulator as VCCD_FPLL and VCCBAT. Decoupling for these pins depends on the design decoupling requirements of the specific board design. | Verify Guidelines have been met or list required actions for compliance. See Notes (3-1) (3-2) (3-3) (3-4) (3-5) (3-7). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCT_GXB[L,R][0:3] (not all pins are available in each device / package combination) |  | Analog power, transmitter, specific to the left (L) side or right (R) side of the device. For Arria V GX -C4, -C5, -I3, -I5, and -C6 devices with data rates <= 3.2Gbps, connect VCCT_GXB pins to a 1.1V low noise switching regulator. For Arria V GX -C4, -C5, -I3, and -I5 devices with data rates > 3.2Gbps, connect VCCT_GXB pins to a 1.15V low noise switching regulator. For Arria V GT devices, connect VCCT_GXB pins to a 1.2V low noise switching regulator. For Arria V GX -C4, -C5, -I5, and -C6 devices with data rates <= 3.2Gbps, these pins may be tied to the same 1.1V regulator as VCC with a proper isolation filter. For Arria V GX -C4, -C5, and -I5 devices with data rates > 3.2Gbps, Arria V GX –I3 devices, and Arria V GT devices, these pins can be tied to the same regulator as VCCL_GXB and VCCR_GXB with proper isolation filter. Decoupling for these pins depends on the design decoupling requirements of the specific board design. | Verify Guidelines have been met or list required actions for compliance. See Notes (3-1) (3-2) (3-3) (3-4) (3-5) (3-7). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCR_GXB[L,R][0:3] (not all pins are available in each device / package combination) |  | Analog power, receiver, specific to the left (L) side or right (R) side of the device. For Arria V GX -C4, -C5, -I3, -I5, and -C6 devices with data rates <= 3.2Gbps, connect VCCR_GXB pins to a 1.1V low noise switching regulator. For Arria V GX -C4, -C5, -I3, and -I5 devices with data rates > 3.2Gbps, connect VCCR_GXB pins to a 1.15V low noise switching regulator. For Arria V GT devices, connect VCCR_GXB pins to a 1.2V low noise switching regulator. For Arria V GX –C4, -C5, -I5, and –C6 devices with data rates <= 3.2Gbps, VCCR_GXB can share the same supply as VCCL_GXB. VCCR_GXB and VCCL_GXB can be shared with the same 1.1V power regulator as VCC with proper isolation filter. For Arria V GX -C4, -C5, and -I5 devices with data rates > 3.2Gbps, Arria V GX –I3 devices, and Arria V GT devices, these pins may be tied to the same regulator as VCCL_GXB. VCCR_GXB and VCCL_GXB can share the same regulator as VCCT_GXB with proper isolation filter. Decoupling for these pins depends on the design decoupling requirements of the specific board design. | Verify Guidelines have been met or list required actions for compliance. See Notes (3-1) (3-2) (3-3) (3-4) (3-5) (3-7). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCL_GXB[L,R][0:3] (not all pins are available in each device / package combination) |  | Analog power, transceiver clock network power, specific to the left (L) side or the right (R) side of the device. For Arria V GX -C4, -C5, -I3, -I5, and -C6 devices with data rates <= 3.2Gbps, connect VCCL_GXB pins to a 1.1V low noise switching regulator. For Arria V GX -C4, -C5, -I3, and -I5 devices with data rates > 3.2Gbps, connect VCCL_GXB pins to a 1.15V low noise switching regulator. For Arria V GT devices, connect VCCL_GXB pins to a 1.2V low noise switching regulator. For Arria V GX –C4, -C5, -I5, and –C6 devices with data rates <= 3.2Gbps, VCCL_GXB can share the same supply as VCCR_GXB. VCCL_GXB and VCCR_GXB can be shared with the same 1.1V power regulator as VCC with proper isolation filter. For Arria V GX -C4, -C5, and -I5 devices with data rates > 3.2Gbps, Arria V GX –I3 devices, and Arria V GT devices, these pins may be tied to the same regulator as VCCR_GXB. VCCL_GXB and VCCR_GXB can share the same regulator as VCCT_GXB with proper isolation filter. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (3-1) (3-2) (3-3) (3-4) (3-5) (3-7). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| REFCLK[0:3] [L,R]_p/n (not all pins are available in each device / package combination) |  | High speed differential reference clock positive and negative receiver channels, specific to the left (L) side or right (R) side of the device. These pins may be AC-coupled or DC-coupled when used. For HCSL I/O standard, it only supports DC-coupling. In the PCI Express configuration, DC-coupling is allowed on the REFCLK if the selected REFCLK I/O standard is HCSL. Connect all unused REFCLK pins directly to GND. | Verify Guidelines have been met or list required actions for compliance. See Note (3-6). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments/ Issues |
| --- | --- | --- | --- |
| GXB_RX_[L,R][0:11]p/n, GXB_REFCLK_[L,R][0:11]p/n (not all pins are available in each device / package combination) |  | High speed positive (p) and negative (n) differential receiver channels, or differential reference clocks. Specific to the left (L) side or right (R) side of the device When used as GXB_RX for data rates > 3.2Gbps, these pins must be AC-coupled. For data rates <= 3.2Gbps, these pins may be AC-coupled or DC-coupled when used as GXB_RX. When used as GXB_REFCLK, these pins must be AC-coupled except when used for PCIe HCSL reference clocks which is the only DC coupling configuration supported. Connect all unused GXB_RXp / GXB_REFCLKp pins directly to GND. Connect all unused GXB_RXn / GXB_REFCLKn pins directly to GND. Some GXB_RX pins have the 10Gbps capability in the Arria V GT device. For details, refer to Transceiver Architecture in Arria V Devices (PDF). | Verify Guidelines have been met or list required actions for compliance. See Note (3-6). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments/ Issues |
| --- | --- | --- | --- |
| GXB_TX_[L,R][0:11]p/n (not all pins are available in each device / package combination) |  | High speed positive (p) or negative (n) differential transmitter channels. Specific to the left (L) side or right (R) side of the device. Leave all unused GXB_TX pins floating. Some GXB_TX pins have the 10Gbps capability in the Arria V GT device. For details, refer to Transceiver Architecture in Arria V Devices (PDF). | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments/ Issues |
| --- | --- | --- | --- |
| RREF_BR |  | Reference resistor for transceiver, specific to the right (R) side of the device, and PLL on bottom and right sides of the device. If any REFCLK pin or transceiver channel on the right side of the device, or PLL on the bottom or right side of the device is used, you must connect the RREF pin on that side of the device to its own individual 2.0-kΩ +/- 1% resistor to GND. Otherwise, you may connect the RREF pin on that side of the device directly to GND. In the PCB layout, the trace from this pin to the resistor needs to be routed so that it avoids any aggressor signals. | Verify Guidelines have been met or list required actions for compliance. |
| RREF_TL |  | Reference resistor for transceiver, specific to the left (L) side of the device, and PLL on top and left side of the device. If any REFCLK pin or transceiver channel on the left side of the device, or PLL on the top or left side of the device is used, you must connect the RREF pin on that side of the device to its own individual 2.0-kΩ +/- 1% resistor to GND. Otherwise, you may connect the RREF pin on that side of the device directly to GND. In the PCB layout, the trace from this pin to the resistor needs to be routed so that it avoids any aggressor signals. |  |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| nPERST[L0,R0] |  | Dedicated fundamental reset pin is only available when used in conjunction with PCIe HIP. One nPERST pin is used per PCIe HIP. The Arria V GX and GT devices always have two pins listed, even if the specific component might have 0 or 1 PCIe hard IP blocks. When this pin is not used as the fundamental reset, this pin may be used as a user I/O pin. Connect this pin as defined in the Quartus II software. When low the transceivers are in reset. When high the transceivers are out of reset. When these pins are not used as the fundamental reset, they may be used as user I/O. nPERSTL0 = Bottom left PCIe HIP and CvP nPERSTR0 = Bottom right PCIe HIP (when available) For maximum compatibility, Altera recommends using nPERSTL0 (the bottom left PCIe HIP) first, this is the only PCIe HIP that supports CvP (Configuration Via Protocol - over the PCIe link). When using the bottom left PCIe HIP, connect nPERST from the PCIe slot directly to nPERSTL0. This pin may be driven by 3.3V regardless of the VCCIO voltage level of the bank without a level translator as long as the input signal meets the LVTTL VIH/VIL specification and the overshoot specifications as listed in the Arria V GX, GT, SX, and ST Device Datasheet (PDF). | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

Notes:

3-1. Capacitance values for the power supply should be selected after consideration of the amount of power they need to supply over the frequency of operation of the particular circuit being decoupled. A target impedance for the power plane should be calculated based on current draw and voltage droop requirements of the device/supply. The power plane should then be decoupled using the appropriate number of capacitors. On-board capacitors do not decouple higher than 100 MHz due to “Equivalent Series Inductance” of the mounting of the packages. Proper board design techniques such as interplane capacitance with low inductance should be considered for higher frequency decoupling.  To assist in decoupling analysis, Altera's Power Delivery Network (PDN) Tool for Arria V Devices serves as an excellent decoupling analysis tool.

3-2. Use the Early Power Estimation Tools to determine the current requirements for VCC and other power supplies.  Power pins should not share breakout vias from the BGA. Each ball on the BGA needs to have its own dedicated breakout via.

3-3. These supplies may share power planes across multiple Arria V devices.

3-4. Low Noise Switching Regulator - defined as a switching regulator circuit encapsulated in a thin surface mount package containing the switch controller, power FETs, inductor, and other support components. The switching frequency is usually between 800kHz and 1MHz and has fast transient response. The switching frequency range is not an Altera requirement. However, Altera does require the Line Regulation and Load Regulation meet the following requirements:

- Line Regulation < 0.4%.

- Load Regulation < 1.2%

3-5. If all of the transceivers on one side of the device are not used, then the transceiver power pins on that side may be tied to GND.  These pins include VCCR_GXB, VCCT_GXB, VCCL_GXB, VCCH_GXB, and VCCA_GXB.  All pins must be powered up or tied to GND.

3-6. For AC-coupled links, the AC-coupling capacitor can be placed anywhere along the channel. PCI Express protocol requires the AC-coupling capacitor to be placed on the transmitter side of the interface that permits adapters to be plugged and unplugged.

3-7. Examples 1 - 15 and Figures 1 - 15 in the Arria V Device Family Pin Connection Guidelines (PDF) illustrate power supply sharing guidelines that are data rate dependent.

Index  Top of Section

Reviewed against Errata Sheet for Arria V Devices (PDF) version:

Additional Comments:

Index  Top of Section

Section IV: I/O

Documentation: Arria V Devices

Arria V Device Pin-Out Files

Arria V Device Family Pin Connection Guidelines (PDF)

Altera Board Design Resource Center (General board design guidelines, PDN design, isolation, tools, and more)

AN 597: Getting Started Flow for Board Designs (PDF)

Errata Sheet and Guidelines for Arria V ES Devices (PDF)

Errata Sheet for Arria V Devices (PDF)

Known Arria V Issues

Index

| Part A: Clock Pins |
| --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| CLK[0:23]p (not all pins are available in each device / package combination) |  | Multi-purpose pins with the following functionality: - Dedicated high speed positive differential clock or differential data input with OCT Rd support. - Single ended clock or data input with OCT Rt support. - Single ended output with OCT Rs support. The programmable weak pull up resistor is available for single ended I/O usage. Use dedicated clock pins to drive clocks into the device. These pins can connect to the device PLLs using dedicated routing paths or global networks. Refer to Clock Networks and PLLs in Arria V devices (PDF) for further information on dedicated routing of clock pins to PLLs. Unused pins can be tied to GND or left unconnected. If unconnected, use the Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| CLK[0:23]n (not all pins are available in each device / package combination) |  | Multi-purpose pins with the following functionality: - Dedicated high speed negative differential clock or differential data input with OCT Rd support. - Single ended clock or data input with OCT Rt support. - Single ended output with OCT Rs support. The programmable weak pull up resistor is available for single ended I/O usage. Use dedicated clock pins to drive clocks into the device. These pins cannot connect to the device PLLs using dedicated routing paths, they use global or regional networks. Refer to Clock Networks and PLLs in Arria V devices (PDF) for further information on dedicated routing of clock pins to PLLs. Unused pins can be tied to GND or left unconnected. If unconnected, use the Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| FPLL_[B,T][L,C,R]_ CLKOUT0, or FPLL_[B,T][L,C,R]_ CLKOUTp, or FPLL_[B,T][L,C,R]_ FB0 (not all pins are available in each device / package combination) |  | Dual purpose I/O pins that can be used as: Two single ended clock output pins, or One differential clock output pair, or Single ended external feedback input pin If not used for their dedicated PLL input or output functionality, these pins are available for regular single ended I/O usage, or as a differential transmitter. Unused pins can be tied to GND or left unconnected. If unconnected, use the Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| FPLL_[B,T][L,C,R]_ CLKOUT1, or FPLL_[B,T][L,C,R]_ CLKOUTn, (not all pins are available in each device / package combination) |  |  |  |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| FPLL_[B,T][L,C,R]_ CLKOUT2, or FPLL_[B,T][L,C,R]_ FBp, or FPLL_[B,T][L,C,R]_ FB1 (not all pins are available in each device / package combination) |  | Dual purpose I/O pins that can be used as: Two single ended clock output pins, or One differential external feedback input pair, or Single ended external feedback input pin If not used for their dedicated PLL feedback input or output functionality, these pins are available for regular single ended I/O usage, or as a differential receiver. Unused pins can be tied to GND or left unconnected. If unconnected, use the Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| FPLL_[B,T][L,C,R]_ CLKOUT3, or FPLL_[B,T][L,C,R]_ FBn (not all pins are available in each device / package combination) |  |  |  |

Index  Top of Section

Additional Comments:

Index  Top of Section

| Part B: Dedicated and Dual Purpose Pins |
| --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| RZQ[0,1,5,6] |  | Calibrated on chip termination reference pins for I/O banks. The RZQ pins share the same VCCIO with the I/O bank where they are located. The external precision resistor must be connected to the designated pin within the bank. When using calibrated OCT tie these pins to GND through either a 240-Ω or 100-Ω resistor, depending on the desired OCT impedance. Refer to I/O Features in Arria V Devices (PDF) for the OCT impedance options for the desired OCT scheme. If not required for its dedicated function, this pin can be used as a regular I/O pin. When not using RZQ# for the external precision resistor or as a regular I/O pin, it is recommended that the pin be connected to GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DNU |  | Do not connect to power or ground or any other signal; these pins must be left unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| NC |  | Do not drive signals into these pins. When designing for device migration these pins may be connected to power, ground, or a signal trace depending on the pin assignment of the devices selected migration. However, if device migration is not a concern leave these pins unconnected. See Knowledge Database solution rd03132006_933. | Verify Guidelines have been met or list required actions for compliance. |

Additional Comments:

Index  Top of Section

| Part C: Dual Purpose Differential I/O pins |
| --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| DIFFIO_RX[T,B][##]p, DIFFIO_RX[T,B][##]n (Refer to the device Pin Table for number of channels based on device selected) |  | These are true LVDS receiver channels on column I/O banks. Pins with a "p" suffix carry the positive signal for the differential channel. Pins with an "n" suffix carry the negative signal for the differential channel. If not used for differential signaling, these pins are available as single ended user I/O pins. These pins do not have dedicated differential transmitters. True LVDS receivers support OCT Rd when VCCPD is 2.5V. Unused pins can be tied to GND or unconnected. If unconnected, use Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DIFFIO_TX[T,B][##]p, DIFFIO_TX[T,B][##]n (Refer to the device Pin Table for number of channels based on device selected) |  | These are true LVDS transmitter channels on column I/O banks. Pins with a "p" suffix carry the positive signal for the differential channel. Pins with an "n" suffix carry the negative signal for the differential channel. If not used for differential signaling, these pins are available as single ended user I/O pins. These pins do not have differential receivers. Unused pins can be tied to GND or unconnected. If unconnected, use Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DIFFOUT_[T,B][##]p, DIFFOUT__[T,B][##]n (Refer to the device Pin Table for number of channels based on device selected) |  | These are emulated LVDS output channels. All user I/Os, including I/Os with true LVDS input buffers, can be configured as emulated LVDS output buffers. Pins with a "p" suffix carry the positive signal for the differential channel. Pins with an "n" suffix carry the negative signal for the differential channel. If not used for differential signaling, these pins are available as single ended user I/O pins. Emulated LVDS transmitters require external resistor networks. Unused pins can be tied to GND or unconnected. If unconnected, use Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

Notes:

4-1. Refer to Knowledge Database solution rd12102002_3281 for further information regarding the concerns when I/O pins are left floating with no internal or external bias.  Ensure there are no conflicts between the Quartus II software device wide default configuration for unused I/Os and the board level connection.  Altera recommends setting unused I/O pins on a project wide basis to behave as inputs tri-state with weak pull up resistor enabled.  Individual unused pins can be reserved with specific behavior such as output driving ground or as output driving VCC to comply with the PCB level connection.

Index  Top of Section

Part D: HPS I/O Pins

This section is used to review the HPS I/O pins for the SoC variants of the Arria V device family (SX and ST). In order for the HPS to operate, the CLKSEL[1..0] and BOOTSEL[2..0] pins must be connected correctly.  For further details, refer to the Configuration section of this review document. For HPS external memory interface pin usage, refer to the External Memory Interfaces section of this review document.

A Quartus II project archive that includes all SoC hard peripherals configured and pinned out as they are intended to be used must be provided for this section of the review.

Each of the HPS I/O pins have multiple dedicated peripheral functions which are listed for each pin in the I/O section of this review.  The I/O pin function on the schematic will be cross referenced to the Quartus II project usage to verify there are no conflicts.  The peripheral pins are programmable through pin multiplexors.  Each pin may have up to four functions, Refer to the Arria V GT, GX, ST, and SX Device Family Pin Connection Guidelines (PDF) for peripheral usage pin function sharing.  Configuration of each pin is done during HPS configuration.

Index  Top of Section

HPS peripheral usage

| Peripheral | Pin multiplexing | Mode |
| --- | --- | --- |
| TRACE |  |  |
| CAN0 |  |  |
| CAN1 |  |  |
| I2C0 |  |  |
| I2C1 |  |  |
| I2C2 |  |  |
| I2C3 |  |  |
| UART0 |  |  |
| UART1 |  |  |
| SPIM0 |  |  |
| SPIM1 |  |  |
| SPIS0 |  |  |
| SPIS1 |  |  |
| SDMMC/SDIO |  |  |
| QSPI |  |  |
| NAND |  |  |
| USB0 |  |  |
| USB1 |  |  |
| EMAC0 |  |  |
| EMAC1 |  |  |

Index Top of Section

| VCCRSTCLK_HPS Voltage: |  |
| --- | --- |

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| HPS_CLK1 |  | The input clock must be present at this pin for HPS operation. Dedicated clock input pin that drives the main PLL. This provides clocks to the MPU, L3/L4 sub-systems, debug sub-system and the Flash controllers. It can also be programmed to drive the peripheral and SDRAM PLLs. Connect a single-ended clock source to this pin. The I/O standard of the clock source must be compatible with VCCRSTCLK_HPS. Refer to the valid frequency range of the clock source in the Arria V Device Datasheet (PDF). The input clock must be present at this pin for HPS operation. | Verify Guidelines have been met or list required actions for compliance. |
| HPS_CLK2 |  | Dedicated clock input pin that can be programmed to drive the peripheral and SDRAM PLLs. Connect a single-ended clock source to this pin. The I/O standard of the clock source must be compatible with VCCRSTCLK_HPS. Refer to the valid frequency range of the clock source in Arria V Device Datasheet (PDF). This is an optional HPS clock input pin. When you do not use this pin, Altera recommends tying it to VCCRSTCLK_HPS. | Verify Guidelines have been met or list required actions for compliance. |

Index Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| HPS_RZQ_0 |  | Reference pin for I/O banks. The HPS_RZQ_0 pin shares the same HPS_VCCIO with the I/O bank where it is located. The external precision resistor must be connected to the designated pin within the bank. If not required, this pin is a regular I/O pin. When this pin is used for the OCT calibration, the HPS_RZQ_0 pin is connected to GND through an external 100-Ω or 240-Ω reference resistor depending on the desired OCT impedance. For the OCT impedance options for the desired OCT scheme, refer to I/O Features In Arria V Devices (PDF). When the Arria V SoC device does not use this dedicated input pin for the external precision resistor or as an I/O pin, Altera recommends connecting this pin to GND. | Verify Guidelines have been met or list required actions for compliance. |
| HPS_GPI[#] (Number of available general purpose input pins is device specific) |  | General purpose inputs signals in the SDRAM bank. These pins use the same VCCIO_HPS as the other HPS SDRAM pins. If unused, configure these pins in the Quartus II software as inputs tristate with weak pull-up resistor enabled. | Verify Guidelines have been met or list required actions for compliance. |

Index Top of Section

TRACE

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| TRACE_CLK |  | TRACE port. Output trace clk. | Verify Guidelines have been met or list required actions for compliance. |
| TRACE_D[7:0] |  | Output trace data. If unused, program it in the Quartus II software as an input with a weak pull-up. | Verify Guidelines have been met or list required actions for compliance. |

CAN0

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| CAN0_RX |  | CAN0 interface. Input Receive Data. | Verify Guidelines have been met or list required actions for compliance. |
| CAN0_TX |  | Output Transmit data. | Verify Guidelines have been met or list required actions for compliance. |

CAN1

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| CAN1_RX |  | CAN1 interface. Input Receive Data. | Verify Guidelines have been met or list required actions for compliance. |
| CAN1_TX |  | Output Transmit data. | Verify Guidelines have been met or list required actions for compliance. |

Index Top of Section HPS Peripheral Table

I2C0

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| I2C0_SDA |  | I2C controller pins. Bidirectional Serial Data. | Verify Guidelines have been met or list required actions for compliance. |
| I2C0_SCL |  | Bidirectional Serial Clock. | Verify Guidelines have been met or list required actions for compliance. |

I2C1

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| I2C1_SDA |  | I2C controller pins. Bidirectional Serial Data. | Verify Guidelines have been met or list required actions for compliance. |
| I2C1_SCL |  | Bidirectional Serial Clock. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section HPS Peripheral Table

I2C2

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| I2C2_SDA |  | I2C controller pins. Bidirectional Serial Data. | Verify Guidelines have been met or list required actions for compliance. |
| I2C2_SCL |  | Bidirectional Serial Clock. | Verify Guidelines have been met or list required actions for compliance. |

I2C3

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| I2C3_SDA |  | I2C controller pins. | Verify Guidelines have been met or list required actions for compliance. |
| I2C3_SCL |  | Bidirectional Serial Clock. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section HPS Peripheral Table

UART0

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| UART0_RX |  | UART controller pins. Input UART receive data. | Verify Guidelines have been met or list required actions for compliance. |
| UART0_TX |  | Output UART transmit data. | Verify Guidelines have been met or list required actions for compliance. |
| UART0_CTS |  | Input UART Clear To Send signal (cts_n). | Verify Guidelines have been met or list required actions for compliance. |
| UART0_RTS |  | Output UART Ready To Send signal (rts_n). | Verify Guidelines have been met or list required actions for compliance. |

UART1

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| UART1_RX |  | UART controller pins. Input UART receive data. | Verify Guidelines have been met or list required actions for compliance. |
| UART1_TX |  | Output UART transmit data. | Verify Guidelines have been met or list required actions for compliance. |
| UART1_CTS |  | Input UART Clear To Send signal (cts_n). | Verify Guidelines have been met or list required actions for compliance. |
| UART1_RTS |  | Output UART Ready To Send signal (rts_n). | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section HPS Peripheral Table

SPIM0

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| SPIM0_CLK |  | SPI master controller pins. Output SPI clock. | Verify Guidelines have been met or list required actions for compliance. |
| SPIM0_MOSI |  | Output SPI Master Out Slave In Data. | Verify Guidelines have been met or list required actions for compliance. |
| SPIM0_MISO |  | Input SPI Master In Slave Out Data. | Verify Guidelines have been met or list required actions for compliance. |
| SPIM0_SS0 |  | Output SPI Slave Select 0. | Verify Guidelines have been met or list required actions for compliance. |
| SPIM0_SS1 |  | Output SPI Slave Select 1. | Verify Guidelines have been met or list required actions for compliance. |

SPIM1

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| SPIM1_CLK |  | SPI master controller pins. Output SPI clock. | Verify Guidelines have been met or list required actions for compliance. |
| SPIM1_MOSI |  | Output SPI Master Out Slave In Data. | Verify Guidelines have been met or list required actions for compliance. |
| SPIM1_MISO |  | Input SPI Master In Slave Out Data. | Verify Guidelines have been met or list required actions for compliance. |
| SPIM1_SS0 |  | Output SPI Slave Select 0. | Verify Guidelines have been met or list required actions for compliance. |
| SPIM1_SS1 |  | Output SPI Slave Select 1. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section HPS Peripheral Table

SPIS0

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| SPIS0_CLK |  | SPI slave controller pins. Input SPI clock. | Verify Guidelines have been met or list required actions for compliance. |
| SPIS0_MOSI |  | Input SPI Master Out Slave In Data. | Verify Guidelines have been met or list required actions for compliance. |
| SPIS0_MISO |  | Output SPI Master In Slave Out Data. | Verify Guidelines have been met or list required actions for compliance. |
| SPIS0_SS0 |  | Input SPI Slave Select. | Verify Guidelines have been met or list required actions for compliance. |

SPIS1

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| SPIS1_CLK |  | SPI slave controller pins. Input SPI clock. | Verify Guidelines have been met or list required actions for compliance. |
| SPIS1_MOSI |  | Input SPI Master Out Slave In Data. | Verify Guidelines have been met or list required actions for compliance. |
| SPIS1_MISO |  | Output SPI Master In Slave Out Data. | Verify Guidelines have been met or list required actions for compliance. |
| SPIS1_SS0 |  | Input SPI Slave Select. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section HPS Peripheral Table

SDMMC/SDIO

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| SDMMC_CMD |  | Where the SD/MMC controller is used these pins form an SD/MMC/CE-ATA interface. Bidirectional card command. | Verify Guidelines have been met or list required actions for compliance. |
| SDMMC_PWREN |  | Output external power enable. | Verify Guidelines have been met or list required actions for compliance. |
| SDMMC_D[7:0] |  | Bidirectional card data. | Verify Guidelines have been met or list required actions for compliance. |
| SDMMC_CLK_IN |  | Input clock to SD/MMC controller CIU. | Verify Guidelines have been met or list required actions for compliance. |
| SDMMC_CLK |  | Output clock to card. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section HPS Peripheral Table

QSPI

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| QSPI_SS[3:0] |  | QSPI controller pins. Output slave select signals. | Verify Guidelines have been met or list required actions for compliance. |
| QSPI_IO[0] |  | Extended SPI mode: Output Data. Dual or quad IO mode: Bidirectional data. | Verify Guidelines have been met or list required actions for compliance. |
| QSPI_IO[1] |  | Extended SPI mode: Input Data. Dual or Quad IO mode: Bidirectional data. | Verify Guidelines have been met or list required actions for compliance. |
| QSPI_IO[2] |  | Extended SPI mode and dual IO mode: Output write protect. Quad IO mode: Bidirectional data. | Verify Guidelines have been met or list required actions for compliance. |
| QSPI_IO[3] |  | Quad IO mode: Bidirectional data. | Verify Guidelines have been met or list required actions for compliance. |
| QSPI_CLK |  | Output clock. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section HPS Peripheral Table

NAND Controller

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| NAND_ALE |  | If the NAND flash controller is used, these pins form the ONFI to a NAND flash device. Output address latch enable. | Verify Guidelines have been met or list required actions for compliance. |
| NAND_CE |  | Output chip enable. | Verify Guidelines have been met or list required actions for compliance. |
| NAND_CLE |  | Output command latch enable. | Verify Guidelines have been met or list required actions for compliance. |
| NAND_RE |  | Output read enable. | Verify Guidelines have been met or list required actions for compliance. |
| NAND_RB |  | Input ready/busy. | Verify Guidelines have been met or list required actions for compliance. |
| NAND_DQ[7:0] |  | Bidirectional command, address, data. | Verify Guidelines have been met or list required actions for compliance. |
| NAND_WP |  | Output write protect. | Verify Guidelines have been met or list required actions for compliance. |
| NAND_WE |  | Output write enable. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section HPS Peripheral Table

USB0

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| USB0_D[7:0] |  | If USB0 is used these pins form the ULPI to a USB PHY. Bidirectional data driven low by the controller during idle. | Verify Guidelines have been met or list required actions for compliance. |
| USB0_CLK |  | Input clock receives the 60MHz clock from the ULPI PHY. | Verify Guidelines have been met or list required actions for compliance. |
| USB0_STP |  | Output stop data control. | Verify Guidelines have been met or list required actions for compliance. |
| USB0_DIR |  | Input data bus control. | Verify Guidelines have been met or list required actions for compliance. |
| USB0_NXT |  | Input next data control. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section HPS Peripheral Table

USB1

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| USB1_D[7:0] |  | If USB1 is used these pins form the ULPI to a USB PHY. Bidirectional data driven low by the controller during idle. | Verify Guidelines have been met or list required actions for compliance. |
| USB1_CLK |  | Input clock receives the 60MHz clock from the ULPI PHY. | Verify Guidelines have been met or list required actions for compliance. |
| USB1_STP |  | Output stop data control. | Verify Guidelines have been met or list required actions for compliance. |
| USB1_DIR |  | Input data bus control. | Verify Guidelines have been met or list required actions for compliance. |
| USB1_NXT |  | Input next data control. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section HPS Peripheral Table

EMAC0

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| RGMII0_TX_CLK |  | If EMAC0 is used, these pins form the RGMII to an Ethernet PHY or switch. Input transmit clock. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII0_RX_CLK |  | Input Receive clock. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII0_TXD[3:0] |  | Output transmit data. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII0_TXCTL |  | Output transmit control. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII0_RXD[3:0] |  | Input Receive data. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII0_RXCTL |  | Input Receive control. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII0_MDC |  | Output management clock. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII0_MDIO |  | Bidirectional management data. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section HPS Peripheral Table

EMAC1

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| RGMII1_TX_CLK |  | If EMAC1 is used, these pins form the RGMII to an Ethernet PHY or switch. Input transmit clock. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII1_RX_CLK |  | Input Receive clock. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII1_TXD[3:0] |  | Output transmit data. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII1_TXCTL |  | Output transmit control. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII1_RXD[3:0] |  | Input Receive data. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII1_RXCTL |  | Input Receive control. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII1_MDC |  | Output management clock. | Verify Guidelines have been met or list required actions for compliance. |
| RGMII1_MDIO |  | Bidirectional management data. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section HPS Peripheral Table

GPIO

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| GPIO[70:0] |  | Pins which are not used for one of the peripheral functions may be used as GPIO. Unused pins can be tied to GND or unconnected. If unconnected, use Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull-up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. |

Index Top of Section HPS Peripheral Table

Reviewed against Errata Sheet for Arria V Devices (PDF) version:

Additional Comments:

Index  Top of Section HPS Peripheral Table

Section V: External Memory Interfaces

Arria V Literature

Arria V Recommended Reference Literature/Tool List

Arria V Pin Out Files

Arria V Device Family Pin Connection Guidelines (PDF)

Altera Board Design Resource Center (General board design guidelines, PDN design, isolation, tools, and more)

Errata Sheet and Guidelines for Arria V ES Devices (PDF)

Errata Sheet for Arria V Devices (PDF)

External Memory Interface Literature

External Memory Interfaces in Arria V Devices (PDF)

DDR2 and DDR3 SDRAM Board Design Guidelines (PDF)

Dual-DIMM DDR2 and DDR3 SDRAM Board Design Guidelines (PDF)

RLDRAM II SRAM Board Design Guidelines (PDF)

QDR II SRAM Board Design Guidelines (PDF)

Planning Pin and FPGA Resources (PDF)

DDR, DDR2, DDR3, QDRII/+ SRAM, RLDRAMII Literature

External Memory interface Handbook

You can use the dedicated memory controllers for DDR2, DDR3 SDRAM, QDRII/+ SRAM and RLDRAMII interfaces.

For pin-outs when implementing Hard Memory Controllers, refer to the Arria V pin-out files. Hard Memory Controller has pre-assigned pins for DDR2 and DDR3 SDRAM along with QDRII/+ SRAM and RLDRAMII interfaces.

Index

| Part A: DDR3/DDR3L Interface Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Data pin - DQ |  | Place it on DQ pins of the DQ/DQS group. The order of the DQ bits within a designated DQ group/bus is not important; however, use caution when making pin assignments if you plan on migrating to a different memory interface that has a different DQ bus width (e.g. migrating from x4 to x8). Analyze the available DQ pins across all pertinent DQS columns in the pin list. | Verify Guidelines have been met or list required actions for compliance. See Note (5-1). |
| Data strobe - DQS/DQSn |  | Should be placed on corresponding DQS and DQSn pins of the DQ/DQS group. | Verify Guidelines have been met or list required actions for compliance. See Notes (5-1) (5-2). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| mem_clk and mem_clk_n |  | Place on any unused DQ or DQS pins with DIFFOUT capability for the mem_clk[n:0] and mem_clk_n[n:0] signals (where n>=0). Do not place CK and CK# pins in the same group as any other DQ or DQS pins. If there are multiple CK and CK# pin pairs, place them on DIFFOUT in the same single DQ group of adequate width. | Verify Guidelines have been met or list required actions for compliance. See Note (5-2). |
| clock_source |  | Input clock pin to the DDR3/ DDR3L core PLL FPGA DDR3/DDR3L interfaces: Dedicated PLL clock input pin with direct (not using a global clock net) connection to the PLL and DLL required by the interface. HPS DDR3/DDR3L interfaces : The SDRAM interface PLL input clock must be sourced from HPS_CLK1 or HPS_CLK2. Altera does not check this. An important recommendation is to use a low jitter clock source. See the recommendations for Memory Output Clock Jitter in the Arria V Datasheet. Altera does not check this. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DM |  | Data Mask Pin – Place it on one of the DQ pins in the group. DM pins need to be part of the DQS/DQ group. | Verify Guidelines have been met or list required actions for compliance. See Note (5-2). |
| Address |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● mem_clk* pins. ● DQ, DQS, or DM pins. | Verify Guidelines have been met or list required actions for compliance. See Note (5-2). |
| Command |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● mem_clk* pins. ● DQ, DQS, or DM pins. | Verify Guidelines have been met or list required actions for compliance. See Note (5-2). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Reset for DDR3/DDR3L Memory |  | Any user I/O pin in the same bank or side of the device as the following pins: ● mem_clk* pins. ● DQ, DQS, or DM pins. | Verify Guidelines have been met or list required actions for compliance. |
| Reset |  | Dedicated clock input pin. (high fan-out signal) The reset pin can alternatively be generated. Ensure the DDR3/DDR3L IP closes reset Recovery/Removal timing in Report DDR. | Verify Guidelines have been met or list required actions for compliance. |
| RZQ |  | Used when calibrated OCT for the memory interface pins is implemented. Make sure that the VCCIO of your DDR3/DDR3L interface bank and the VCCIO of the bank with RZQ pin match. If the RZQ pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

5-1. DDR3 and DDR3L only support differential DQS signaling.

5-2. Arria V GX Hard Memory Interfaces and Arria V SoC HPS SDRAM Interfaces have pre-assigned pins for DDR3/DDR3L SDRAM interfaces.

Index  Top of Section

Additional Comments:

Index  Top of Section

| Part B: DDR3DDR3L Interface Termination Guidelines |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Memory clocks@ Memory |  | Arria V devices do not support DDR3/DDR3L SDRAM with read or write leveling, so these devices do not support standard DDR3/DDR3L SDRAM DIMMs or DDR3/DDR3L SDRAM components using the standard DDR3/DDR3L SDRAM fly-by address, command, and clock layout topology. Devices (without leveling) – differential termination resistor needs to be included in the design. Depending on your board stackup and layout requirements, you choose your differential termination resistor value. | Verify Guidelines have been met or list required actions for compliance. See Note (5-3). |
| Memory clocks@ FPGA |  | DDR3 : Use series 50-Ω output termination without calibration. DDR3L : Use series 40-Ω output termination without calibration. Source <variation_name>_pin_assignments.tcl to make the setting. | Verify Guidelines have been met or list required actions for compliance. See Note (5-3). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DQS @ Memory |  | Use ODT. | Verify Guidelines have been met or list required actions for compliance. See Note (5-3). |
| DQS @ FPGA |  | DDR3 : Use parallel 50-Ω with calibration as input termination and series 50-Ω with calibration as output termination. DDR3L : Use parallel 40-Ω with calibration as input termination and series 40-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-3). |
| DQ @ Memory |  | Use ODT. | Verify Guidelines have been met or list required actions for compliance. See Note (5-3). |
| DQ @ FPGA |  | DDR3 : Use parallel 50-Ω with calibration as input termination and series 50-Ω with calibration as output termination. DDR3L : Use parallel 40-Ω with calibration as input termination and series 40-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to assign these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-3). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DM@ Memory |  | Use ODT. If DM pins are unused, refer to the DDR3/DDR3L manufacturer's data sheet for connection recommendations. Typically they must be tied low using a resistor no greater than 4*Rtt (the nominal ODT value used on the memory device). | Verify Guidelines have been met or list required actions for compliance. See Note (5-3). |
| DM @ FPGA |  | DDR3 : Use series 50-Ω with calibration as output termination. DDR3L : Use series 40-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-3). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Address [BA, mem_addr] @ Memory |  | Discrete Device (no leveling) - Unidirectional class I termination. Unidirectional class I termination. For multi-loads Altera recommends the ideal topology is a balanced symmetrical tree. Altera recommends that the class I termination to VTT is placed at the first split or division of the symmetrical tree for discrete devices. | Verify Guidelines have been met or list required actions for compliance. See Note (5-3). |
| Address [BA, mem_addr] @ FPGA |  | DDR3 : Use maximum current drive strength. DDR3L : Use series 40-Ω without calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-3). |
| Command [CKE, CS_N, ODT, RAS, CAS, WE_N] @ Memory |  | Discrete Device (no leveling) - Unidirectional class I termination. Unidirectional class I termination. For multi-loads Altera recommends the ideal topology is a balanced symmetrical tree. Altera recommends that the class I termination to VTT is placed at the first split or division of the symmetrical tree for discrete devices. | Verify Guidelines have been met or list required actions for compliance. See Note (5-3). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Command [CKE, CS_N, ODT, RAS, CAS, WE_N] @ FPGA |  | DDR3 : Use maximum current drive strength. DDR3L : Use series 40-Ω without calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-3). |
| Reset for DDR3/DDR3L Memory |  | DDR3 : Use 1.5V CMOS output. DDR3L : Use SSTL-135 output It is not recommended to terminate this reset to Vtt. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

5-3. The termination schemes suggested in the table are general guidelines. You should do board level simulation for your particular system/board to determine optimal termination scheme.

Additional Comments:

Index  Top of Section

| Miscellaneous |  |  |  |
| --- | --- | --- | --- |
| Pin Description | Schematic Name | Connection Guidelines | Comments / Issues |
| Vref |  | Use a voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. |
| Vtt |  | Use a voltage regulator to generate this voltage. Typically DDR3/DDR3L DIMMS have decoupling capacitors connected between VTT and VDD and it is recommended that designers follow this approach. Note that DDR3/DDR3L DIMM layout topology is not supported. | Verify Guidelines have been met or list required actions for compliance. |
| RZQ |  | RZQ pin is connected to GND through an external 240-Ω or 100-Ω ±1% resistor. Refer to I/O Features in Arria V Devices (PDF) for the OCT impedance options for the desired OCT scheme. If the RZQ pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Additional Comments:

Index  Top of Section

| Part C: DDR2 Interface Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Data pins - DQ |  | Place it on DQ pins of the DQ/DQS group. The order of the DQ bits within a designated DQ group/bus is not important; however, use caution when making pin assignments if you plan on migrating to a different memory interface that has a different DQ bus width (e.g. migrating from x4 to x8). Analyze the available DQ pins across all pertinent DQS columns in the pin list. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |
| Data strobe - DQS/DQSn |  | Differential DQS - Should be placed on corresponding DQS and DQSn pins of the DQ/DQS group. Single ended DQS – Connect the DQS pin to the DQS pin of the corresponding DQ/DQS group. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |
| Data Mask DM |  | Place it on one of the DQ pins in the group. DM pins need to be part of the write DQS/DQ group. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| mem_clk[n:0] and mem_clk_n[n:0] |  | If you are using single-ended DQS signaling, place any unused DQ or DQS pins with DIFFOUT capability in the same bank or on the same side as the data pins. If you are using differential DQS signaling, place any unused DQ or DQS pins with DIFFOUT capability for the mem_clk[n:0] and mem_clk_n[n:0] signals (where n>=0). Do not place CK and CK# pins in the same group as any other DQ or DQS pins. If there are multiple CK and CK# pin pairs, place them on DIFFOUT in the same single DQ group of adequate width. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| clock_source |  | Input clock pin to the DDR2 core PLL – FPGA DDR2 interface: Dedicated PLL clock input pin with direct (not using a global clock net) connection to the PLL and DLL required by the interface. HPS DDR2 interface : The SDRAM interface PLL input clock must be sourced from HPS_CLK1 or HPS_CLK2. Altera does not check this. An important recommendation is to use a low jitter clock source. See the recommendations for Memory Output Clock Jitter in the Arria V Datasheet. Altera does not check this. | Verify Guidelines have been met or list required actions for compliance. |
| Address |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● mem_clk* pins. ● DQ, DQS, or DM pins. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |
| Command |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● mem_clk* pins. ● DQ, DQS, or DM pins. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Reset |  | Dedicated clock input pin. (high fan-out signal) The reset pin can alternatively be generated. Ensure the DDR3 IP closes reset Recovery/Removal timing in Report DDR. | Verify Guidelines have been met or list required actions for compliance. |
| RZQ |  | Used for the implementation of calibrated OCT for the memory interface pins. RZQ should be in any 1.8V VCCIO bank. Make sure that the VCCIO of your DDR2 interface bank and the VCCIO of the bank with RZQ pin match. If the RZQ pins are used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

5-4. Arria V GX Hard Memory Interfaces and Arria V SoC HPS SDRAM  Interfaces have pre-assigned pins for DDR2 SDRAM interfaces.

Additional Comments:

Index  Top of Section

| Part D: DDR2 Termination Guidelines |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Memory clocks @ Memory |  | Memory clocks use Unidirectional class I termination. They are typically differentially terminated with an effective 100-Ω resistance. For DIMM no termination is required as termination is placed on the DIMM itself. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| Memory clocks@ FPGA |  | Use series 50-Ω output termination without calibration on the FPGA side. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| DQS @ Memory |  | Use ODT for DDR2. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| DQS @ FPGA |  | Use parallel 50-Ω with calibration as input termination. Use series 50-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| DQ @ Memory |  | Use ODT for DDR2. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DQ @ FPGA |  | Use parallel 50-Ω with calibration as input termination. Use series 50-Ω with calibration as output termination. Source<variation_name>_pin_assignments.tcl file to assign these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. |
| DM@ Memory |  | Use ODT for DDR2. If DM pins are unused, refer to the DDR2 manufacturer's data sheet for connection recommendations. Typically they must be tied low using a resistor no greater than 4*Rtt (the nominal ODT value used by the memory device). | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| DM @ FPGA |  | Use series 50-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Address [BA, mem_addr] @ Memory |  | Unidirectional class I termination. For multi-loads Altera recommends the ideal topology is a balanced symmetrical tree. Altera recommends that the class I termination to VTT is placed: ■ At the DIMM connector (for interfaces using DIMMs). ■ At the first split or division of the symmetrical tree for discrete devices. Nonsymmetrical topologies or DIMMs result in over or undershoot and oscillations on the line, which may require compensation capacitors or a lower than ideal drive strength to be specified resulting in de-rated interface performance. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| Address [BA, mem_addr] @ FPGA |  | Use maximum current strength as the output drive strength. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Command [CKE, CS_N, ODT, RAS, CAS, WE_N]@ Memory |  | Unidirectional class I termination. For multi-loads Altera recommends the ideal topology is a balanced symmetrical tree. Altera recommends that the class I termination to VTT is placed: ■ At the DIMM connector (for interfaces using DIMMs). ■ At the first split or division of the symmetrical tree for discrete devices. Nonsymmetrical topologies or DIMMs result in over or undershoot and oscillations on the line, which may require compensation capacitors or a lower than ideal drive strength to be specified resulting in de-rated interface. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| Command [CKE, CS_N, ODT, RAS, CAS, WE_N]@ FPGA |  | Use maximum current strength as the output drive strength. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

5-5. The termination schemes suggested in the table are general guidelines. You should do board level simulation for your particular system/board to determine optimal termination scheme.

Index  Top of Section

| Miscellaneous |  |  |  |
| --- | --- | --- | --- |
| Pin Description | Schematic Name | Connection Guidelines | Comments/ Issues |
| Vref |  | Use voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. See Note (5-6). |
| Vtt |  | Use voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. See Note (5-6). |
| RZQ |  | RZQ pin is connected to GND through an external 240-Ω or 100-Ω ±1% resistor. Refer to I/O Features in Arria V Devices (PDF) for the OCT impedance options for the desired OCT scheme. If the RZQ pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

5-6. This worksheet does not calculate required decoupling, it is expected the designer will select decoupling based on analysis of power required and impedance of power path required based on static and switching current values.  Refer to Altera’s Power Delivery Network (PDN) Tool for Arria V Devices for further information.

Capacitance values for the power supply should be selected after consideration of the amount of power they need to supply over the frequency of operation of the particular circuit being decoupled. A target impedance for the power plane should be calculated based on current draw and voltage drop requirements of the device/supply. The power plane should then be decoupled using the appropriate number of capacitors. On-board capacitors do not decouple higher than 100 MHz due to “Equivalent Series Inductance” of the mounting of the packages. Proper board design techniques such as interplane capacitance with low inductance should be considered for higher frequency decoupling.

Index  Top of Section

Additional Comments:

Index  Top of Section

| Part E: LPDDR2 Interface Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Data pins - DQ |  | Place it on DQ pins of the DQ/DQS group. The order of the DQ bits within a designated DQ group/bus is not important. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| Data strobe - DQS/DQSn |  | Differential DQS - Should be placed on corresponding DQS and DQSn pins of the DQ/DQS group. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| Data Mask DM |  | Place it on one of the DQ pins in the group. DM pins need to be part of the write DQ/DQS group. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| mem_ck[n:0] and mem_ck_n[n:0] |  | Place on any unused DQ or DQS pins with DIFFOUT capability for the mem_clk[n:0] and mem_clk_n[n:0] signals (where n>=0). Do not place CK and CK# pins in the same group as any other DQ or DQS pins. If there are multiple CK and CK# pin pairs, place them on DIFFOUT in the same single DQ group of adequate width. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| clock_source |  | Input clock pin to the LPDDR2 core PLL – FPGA LPDDR2 interface: Dedicated PLL clock input pin with direct (not using a global clock net) connection to the PLL and DLL required by the interface. HPS LPDDR2 interface : The SDRAM interface PLL input clock must be sourced from HPS_CLK1 or HPS_CLK2. Altera does not check this. An important recommendation is to use a low jitter clock source. See the recommendations for Memory Output Clock Jitter in the Arria V Datasheet. Altera does not check this. | Verify Guidelines have been met or list required actions for compliance. |
| Address/Command |  | The LPDDR2 command code includes the address, cs_n and cke signals. Any DDR-capable I/O pin. DDR capable pins include pins that are in a DQ/DQS group and the 4 additional pins that make up the 16 pin group. Refer to the device pin tables for further information. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins : ● CK/CK# ● DQ. DQS, or DM pins. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Reset |  | Dedicated clock input pin. (high fan-out signal) The reset pin can alternatively be generated. Ensure the LPDDR2 IP closes reset Recovery/Removal timing in Report DDR. | Verify Guidelines have been met or list required actions for compliance. |
| RZQ |  | Used for the implementation of calibrated OCT for the memory interface pins. RZQ should be in any 1.2V VCCIO bank. Make sure that the VCCIO of your LPDDR2 interface bank and the VCCIO of the bank with RZQ pin match. If the RZQ pins are used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

5-7. Arria V GX Hard Memory Interfaces and Arria V SoC HPS SDRAM  Interfaces have pre-assigned pins for DDR2 SDRAM interfaces

Additional Comments:

Index  Top of Section

| Part F: LPDDR2 Termination Guidelines |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Memory clocks @ Memory |  | Memory clocks use Unidirectional class I termination. They are typically differentially terminated with an effective 100-Ω resistance. | Verify Guidelines have been met or list required actions for compliance. See Note (5-8). |
| Memory clocks@ FPGA |  | Use series 34-Ω output termination with calibration on the FPGA side. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-8). |
| DQS @ Memory |  | LPDDR2 does not use ODT. Typically an LPDDR2 memory component has a 240 ohm resistor connected between its ZQ pin and GND or VDDCA to allow mode register programming of the driver output impedance. Refer to the LPDDR2 SDRAM data sheet for further information. | Verify Guidelines have been met or list required actions for compliance. See Note (5-8). |
| DQS @ FPGA |  | Use series 34-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-8). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DQ @ Memory |  | LPDDR2 does not use ODT. Typically an LPDDR2 memory component has a 240 ohm resistor connected between its ZQ pin and GND or VDDCA to allow mode register programming of the driver output impedance. Refer to the LPDDR2 SDRAM data sheet for further information. | Verify Guidelines have been met or list required actions for compliance. See Note (5-8). |
| DQ @ FPGA |  | Use series 34-Ω with calibration as output termination. Source<variation_name>_pin_assignments.tcl file to assign these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. |
| DM@ Memory |  | LPDDR2 does not use ODT. No termination is recommended at the memory component. | Verify Guidelines have been met or list required actions for compliance. See Note (5-8). |
| DM @ FPGA |  | Use series 34-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Address/Command [CA, CS_N, CKE] @ Memory |  | Parallel termination is not recommended to save power. For multi-loads Altera recommends the ideal topology is a balanced symmetrical tree. Nonsymmetrical topologies may result in over or undershoot and oscillations on the line, which may require compensation capacitors or a lower than ideal drive strength to be specified resulting in de-rated interface performance. For CKE, a 4.7K resistor to GND is recommended if your design meets the power sequencing requirements of the LPDDR2 SDRAM component. Refer to the LPDDR2 SDRAM data sheet for further information. | Verify Guidelines have been met or list required actions for compliance. See Note (5-8). |
| Address/Command [CA, CS_N, CKE] @ Memory |  | Use series 34-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

5-8. The termination schemes suggested in the table are general guidelines. You should do board level simulation for your particular system/board to determine optimal termination scheme. As many signals are not recommended use parallel terminations at the receiving end of the line to save power, it is strongly recommended to perform board level simulations to verify the signal integrity of your interface.

Index Top of Section

| Miscellaneous |  |  |  |
| --- | --- | --- | --- |
| Pin Description | Schematic Name | Connection Guidelines | Comments/ Issues |
| Vref |  | Use voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. See Note (5-9). |
| Vtt |  | Use voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. See Note (5-9). |
| RZQ |  | RZQ pin is connected to GND through an external 240-Ω or 100-Ω ±1% resistor. Refer to I/O Features in Arria V Devices (PDF) for the OCT impedance options for the desired OCT scheme. If the RZQ pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

5-9. This worksheet does not calculate required decoupling, it is expected the designer will select decoupling based on analysis of power required and impedance of power path required based on static and switching current values.  Refer to Altera’s Power Delivery Network (PDN) Tool for Arria V Devices for further information.

Capacitance values for the power supply should be selected after consideration of the amount of power they need to supply over the frequency of operation of the particular circuit being decoupled. A target impedance for the power plane should be calculated based on current draw and voltage drop requirements of the device/supply. The power plane should then be decoupled using the appropriate number of capacitors. On-board capacitors do not decouple higher than 100 MHz due to “Equivalent Series Inductance” of the mounting of the packages. Proper board design techniques such as interplane capacitance with low inductance should be considered for higher frequency decoupling.

Index  Top of Section

Additional Comments:

Index  Top of Section

| Part G: QDR II/+ Interface Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Q – Read data pins |  | Assign it to the DQ pins of an available DQ/DQS pin group. The order of the DQ bits within a designated DQ group/bus is not important; however, use caution when making pin assignments if you plan on migrating to a different memory interface that has a different DQ bus width. Analyze the available DQ pins across all pertinent DQS columns in the pin list. | Verify Guidelines have been met or list required actions for compliance. See Note (5-10). |
| D – Write data pins |  | Assign it to the DQ pins of an available DQ/DQS pin group. The order of the DQ bits within a designated DQ group/bus is not important; however, use caution when making pin assignments if you plan on migrating to a different memory interface that has a different DQ bus width. Analyze the available DQ pins across all pertinent DQS columns in the pin list. | Verify Guidelines have been met or list required actions for compliance. See Note (5-10). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Read clock to the FPGA - CQ/CQn |  | For QDR II SRAM devices with 1.5 or 2.5 cycles of read latency or QDR II+ SRAM devices with 2.5 cycles of read latency, connect CQ to DQS pin, and CQn to CQn pin. For QDR II or QDR II+ SRAM devices with 2.0 cycles of read latency, connect CQ to CQn pin, and CQn to DQS pin. | Verify Guidelines have been met or list required actions for compliance. See Note (5-10). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Write clock from the FPGA - K/Kn |  | K – Place it on DQS pin. Kn –Place it on DQSn They have to be placed in the write data group. | Verify Guidelines have been met or list required actions for compliance. See Note (5-10). |
| Input clock for output data – C and Cn |  | Altera QDRII SRAM interface is implemented in single clock mode. Connect C and Cn high. Also, look for the connection guidance in the memory device datasheet. | Verify Guidelines have been met or list required actions for compliance. See Note (5-10). |
| QVLD |  | QVLD signal indicates that the read data coming to the FPGA is ready to be captured. Place it in the read DQS/DQ group. Only QDRII+ SRAM device has a QVLD. UniPHY IP does not use QVLD signal. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| clock_source |  | Input clock pin to the QDRII/+ core PLL - Dedicated PLL clock input pin with direct (not using a global clock net) connection to the PLL and DLL required by the interface. An important recommendation is to use a low jitter clock source. See the recommendations for Memory Output Clock Jitter in the Arria V Datasheet. Altera does not check this. | Verify Guidelines have been met or list required actions for compliance. |
| BWSn |  | Data Mask Pin – Place it on one of the DQ pins in the group. BWSn pins need to be part of the write DQS/DQ group. | Verify Guidelines have been met or list required actions for compliance. See Note (5-10). |
| Address |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● Clock pins. ● Data pins If you are using burst-length-of-two devices, To optimize timing, it is recommended to place the address signals on a DQS group pin as these signals are now double data rate. | Verify Guidelines have been met or list required actions for compliance. See Note (5-10). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Command |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● Clock pins. ● Data pins If you are using burst-length-of-two devices, To optimize timing, it is recommended to place the address signals on a DQS group pin as these signals are now double data rate. | Verify Guidelines have been met or list required actions for compliance. See Note (5-10). |
| Reset |  | Dedicated clock input pin. (high fan-out signal). Reset signal can also be generated internally in your design. Ensure the DDR3 IP closes reset Recovery/Removal timing in Report DDR. | Verify Guidelines have been met or list required actions for compliance. |
| d_off |  | Refer to memory specification and guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| RZQ |  | Used when calibrated OCT for the memory interface pins is implemented. RZQ should be in any 1.5V / 1.8V VCCIO bank. Make sure that the VCCIO of your QDRII interface bank and the VCCIO of the bank with the RZQ pin match. If the RZQ pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

5-10. Arria V GX Hard Memory Interfaces have pre-assigned pins for QDRII/+ SRAM interfaces.

Additional Comments:

Index  Top of Section

| Part H: QDRII/+ Termination Guidelines |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Write Clock (K/Kn) @ FPGA |  | Class I termination scheme. FPGA side termination is implemented through OCT feature so that no board level termination required on the FPGA side. For the write clock signals Altera recommends series OCT 50-Ω with calibration. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |
| Write Clock (K/Kn) @ Memory |  | Class I termination scheme. Write clock at the memory side should be terminated with class I Parallel termination at the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |
| Read Clock (CQ/CQn) @ FPGA |  | For the read clock signals Altera recommends using parallel OCT 50-Ω with calibration. If x36 emulated mode being used, then it is recommended to terminate the split CQ/CQn clocks externally and not use the FPGA OCT. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Read Clock (CQ/CQn) @ Memory |  | Read clock output impedance is implemented with the help of ZQ input pin on the memory device side. If not, you need to put 50-Ω series OCT on the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |
| Write data - D @ FPGA |  | Use series 50-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |
| Write data – D @ Memory |  | Write data at the memory side should be terminated with class I Parallel termination at the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Read data - Q @ FPGA |  | Use parallel 50-Ω with calibration as input termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |
| Read data - Q @ Memory |  | Read data output impedance is implemented with the help of ZQ input pin on the memory device side. If not, you need to put 50-Ω series OCT on the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |
| BWSn @ FPGA |  | Use series 50-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |
| BWSn @ Memory |  | BWSn at the memory side should be terminated with class I Parallel termination at the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |
| QVLD @ FPGA |  | Use parallel 50-Ω with calibration as input termination. If x36 emulated mode is being used, then it is recommended to terminate the split on QVLD signal externally and not use the FPGA OCT. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Address @ FPGA |  | If there are multiple loads on certain FPGA output pins (for example, if the address bus is shared across many memory devices), use of maximum drive strength setting may be preferred over the series OCT setting. Use board level simulations to pick the optimal setting for best signal integrity. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |
| Address @ Memory |  | On the memory side, Altera recommends the use of external parallel termination on input signals to the memory. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |
| Command @ FPGA |  | If there are multiple loads on certain FPGA output pins (for example, if the address bus is shared across many memory devices), use of maximum drive strength setting may be preferred over the series OCT setting. Use board level simulations to pick the optimal setting for best signal integrity. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |
| Command @ Memory |  | On the memory side, Altera recommends the use of external parallel termination on input signals to the memory. | Verify Guidelines have been met or list required actions for compliance. See Note (5-11). |

Index  Top of Section

Miscellaneous:

| Pin Description | Schematic Name | Connection Guidelines | Comments/Issues |
| --- | --- | --- | --- |
| Vref |  | Use a voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. See Note (5-12). |
| Vtt |  | Use a voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. See Note (5-12). |
| RZQ |  | RZQ pin is connected to GND through an external 240-Ω or 100-Ω ±1% resistor. Refer to I/O Features in Arria V Devices (PDF) for the OCT impedance options for the desired OCT scheme. If the RZQ pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

Notes:

5-11. The termination schemes suggested in the table are general guidelines. You should do board level simulation for your particular system/board to determine optimal termination scheme.

5-12. This worksheet does not calculate required decoupling, it is expected the designer will select decoupling based on analysis of power required and impedance of power path required based on static and switching current values.  Refer to Altera’s Power Delivery Network (PDN) Tool for Arria V Devices for further information.

Capacitance values for the power supply should be selected after consideration of the amount of power they need to supply over the frequency of operation of the particular circuit being decoupled. A target impedance for the power plane should be calculated based on current draw and voltage drop requirements of the device/supply. The power plane should then be decoupled using the appropriate number of capacitors. On-board capacitors do not decouple higher than 100 MHz due to “Equivalent Series Inductance” of the mounting of the packages. Proper board design techniques such as interplane capacitance with low inductance should be considered for higher frequency decoupling.

Additional Comments:

Index  Top of Section

Reviewed against Errata Sheet for Arria V Devices (PDF) version:

Additional Comments:

Index  Top of Section

Section VI: Document Revision History

| Revision | Changes Made | Date |
| --- | --- | --- |
| V4.0 | Synchronized with Arria V GT, GX, ST, and SX Device Family Pin Connection Guidelines version 1.9. Removed reference to GXB_TX pins supporting AC coupled links only. Changed Note 3-7 to include all examples and figures. Added DDR3L guidelines to DDR3 section. Added HPS specific guidelines to DDR3/3L, DDR2, and LPDDR2 sections. Added LPDDR2 Interface Pins and Termination Guidelines sections. | April 2014 |
| V3.0 | Synchronized with Arria V GT, GX, ST, and SX Device Family Pin Connection Guidelines version 1.8. Added HPS device (SX and ST) connection guidelines. Updated CLKUSR connection guideline to set as output driving GND in the Quartus II software. Removed requirement for VCCIO to be 2.5V on DIFFIO_RX pins to support OCT Rd. Changed VCCAUX to VCC_AUX and updated VCC_AUX connection guideline. | August 2013 |
| V2.0 | Synchronized with Arria V GT and GX Device Family Pin Connection Guidelines version 1.6. Updated transceiver reference material links. Added note 3-3 to VCCR_GXB, VCCT_GXB, and VCCL_GXB. Added note 1-5 to power section. Updated nPERST and REFCLK connection guidelines. Updated description for VCCL_GXB. Updated notes 1-3, 3-4, and 3-5. | May 2013 |
| V1.2 | Synchronized with Arria V Device Family Pin Connection Guidelines version 1.5. Updated the data rate from 3.125Gbps to 3.2Gbps for VCCL_GXB, VCCR_GXB, and VCCT_GXB pins Updated GXB_RX_[L,R] connection guidelines to allow for DC coupling for data rates <= 3.2Gbps | December 2012 |
| V1.1 | Synchronized with Arria V Device Family Pin Connection Guidelines version 1.4. Updated GXB_RX, GXB_TX, and GXB_REFCLK guidelines for AC coupling usage. Added Arria V GX I3 information. Updated VCCD_FPLL and RREF connection guidelines to show fPLL functional dependency on RREF connection. Added clarification to the DCLK and VCCP connection guidelines. | October 2012 |
| V1.0 | Initial release, based on the Arria V Device Family Pin Connection Guidelines version 1.3. | June 2012 |

Index