Stratix® II Device Schematic Review Worksheet

This document is intended to help you review your schematic and compare the pin usage against the Stratix II GX Device Family Pin Connection Guidelines (PDF) version 3.1 and other referenced literature for this device family.  The technical content is divided into focus areas such as FPGA power supplies, configuration, FPGA I/O, and external memory interfaces.

Within each focus area, there is a table that contains the voltage or pin name for all of the dedicated and dual purpose pins for the device family.  In some cases, the device density and package combination may not include some of the pins shown in this worksheet, you should cross reference with the pin-out file for your specific device.  Links to the device pin-out files are provided at the top of each section.

Before you begin using this worksheet to review your schematic and commit to board layout, Altera highly recommends:

1) Review the latest version of the Stratix II FPGA Family Errata Sheet (PDF) and the Knowledge Database for Stratix II Device Known Issues and Stratix II  Device Handbook Known Issues.

2)  Compile your design in the Quartus® II software to completion.

For example, there are many I/O related placement restrictions and VCCIO requirements for the I/O standards used in the device.  If you do not have a complete project, then at a minimum a top level project should be used with all I/O pins defined, placed, and apply all of the configurable options that you plan to use.  All I/O related megafunctions should also be included in the minimal project, including, but not limited to, external memory interfaces, PLLs, altlvds, and altddio.  The I/O Analysis tool in the Pin Planner can then be used on the minimal project to validate the pinout in Quartus II software to assure there are no conflicts with the device rules and guidelines.

When using the I/O Analysis tool you must ensure there are no errors with your pinout.  Additionally, you should check all warning and critical warning messages to evaluate their impact on your design.  You can right click your mouse over any warning or critical warning message and select “Help”.  This will bring open a new Help window with further information on the cause of the warning, and the action that is required.

For example, the following warning is generated when a PLL is driven by a global network where the source is a valid dedicated clock input pin, but the pin is not one dedicated to the particular PLL:

Warning: PLL "<PLL Instance Name>" input clock inclk[0] is not fully compensated and may have reduced jitter performance because it is fed by a non-dedicated input

Info: Input port INCLK[0] of node "<PLL Instance Name>" is driven by clock~clkctrl which is OUTCLK output port of Clock Control Block type node clock~clkctrl

The help file provides the following:

| CAUSE: | The specified PLL's input clock is not driven by a dedicated input pin. As a result, the input clock delay will not be fully compensated by the PLL. Additionally, jitter performance depends on the switching rate of other design elements. This can also occur if a global signal assignment is applied to the clock input pin, which forces the clock to use the non-dedicated global clock network. |
| --- | --- |
| ACTION: | If you want compensation of the specified input clock or better jitter performance, connect the input clock only to an input pin, or assign the input pin only to a dedicated input clock location for the PLL. If you do not want compensation of the specified input clock, then set the PLL to No Compensation mode. |

When assigning the input pin to the proper dedicated clock pin location, refer to PLLs in Stratix and Stratix II GX Devices (PDF) for the proper port mapping of dedicated clock input pins to PLLs.

There are many reports available for use after a successful compilation or I/O analysis.  For example, you can use the “All Package Pins” and “I/O Bank Usage” reports within the Compilation – Fitter – Resource Section to see all of the I/O standards and I/O configurable options that are assigned to all of the pins in your design, as well as view the required VCCIO for each I/O bank.  These reports must match your schematic pin connections.

The review table has the following heading:

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |

The first column (Plane/Signal) lists the FPGA voltage or signal pin name.  You should only edit this column to remove dedicated or dual purpose pin names that are not available for your device density and package option.

The second column (Schematic Name) is for you to enter your schematic name(s) for the signal(s) or plane connected to the FPGA pin(s).

The third column (Connection Guidelines) should be considered “read only” as this contains Altera’s recommended connection guidelines for the voltage plane or signal.

The fourth column (Comments/Issues) is an area provided as a “notepad” for you to comment on any deviations from the connection guidelines, and to verify guidelines are met.  In many cases there are notes that provide further information and detail that compliment the connection guidelines

Here is an example of how the worksheet can be used:

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| <Plane / Signal name provided by Altera> VCCINT | <user entered text> +1.2V | <Device Specific Guidelines provided by Altera> | <user entered text> Connected to +1.2V plane, no isolation is necessary. Missing low and medium range decoupling, check PDN. See Notes (1-1) (1-2). |

Legal Note:

PLEASE REVIEW THE FOLLOWING TERMS AND CONDITIONS CAREFULLY BEFORE USING THIS SCHEMATIC REVIEW WORKSHEET (“WORKSHEET”) PROVIDED TO YOU. BY USING THIS WORKSHEET, YOU INDICATE YOUR ACCEPTANCE OF SUCH TERMS AND CONDITIONS, WHICH CONSTITUTE THE LICENSE AGREEMENT ("AGREEMENT") BETWEEN YOU AND ALTERA CORPORATION OR ITS APPLICABLE SUBSIDIARIES ("ALTERA").

1. Subject to the terms and conditions of this Agreement, Altera grants to you, for no additional fee, a non-exclusive and non-transferable right to use this Worksheet for the sole purpose of verifying the validity of the pin connections of an Altera programmable logic device-based design. You may not use this Worksheet for any other purpose.  There are no implied licenses granted under this Agreement, and all rights, except for those granted under this Agreement, remain with Altera.

2. Altera does not guarantee or imply the reliability, or serviceability, of this Worksheet or other items provided as part of this Worksheet. This Worksheet is provided 'AS IS'. ALTERA DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING THE IMPLIED WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, AND NON-INFRINGEMENT.  ALTERA HAS NO OBLIGATION TO PROVIDE YOU WITH ANY SUPPORT OR MAINTENANCE.

3. In no event shall the aggregate liability of Altera relating to this Agreement or the subject matter hereof under any legal theory (whether in tort, contract, or otherwise), exceed One Hundred US Dollars (US$100.00). In no event shall Altera be liable for any lost revenue, lost profits, or other consequential, indirect, or special damages caused by your use of this Worksheet even if advised of the possibility of such damages.

4. This Agreement may be terminated by either party for any reason at any time upon 30-days’ prior written notice.  This Agreement shall be governed by the laws of the State of California, without regard to conflict of law or choice of law principles. You agree to submit to the exclusive jurisdiction of the courts in the County of Santa Clara, State of California for the resolution of any dispute or claim arising out of or relating to this Agreement. The parties hereby agree that the party who is not the substantially prevailing party with respect to a dispute, claim, or controversy relating to this Agreement shall pay the costs actually incurred by the substantially prevailing party in relation to such dispute, claim, or controversy, including attorneys' fees.  Failure to enforce any term or condition of this Agreement shall not be deemed a waiver of the right to later enforce such term or condition or any other term or condition of the Agreement.

BY USING THIS WORKSHEET, YOU ACKNOWLEDGE THAT YOU HAVE READ THIS AGREEMENT, UNDERSTAND IT, AND AGREE TO BE BOUND BY ITS TERMS AND CONDITIONS. YOU AND ALTERA FURTHER AGREE THAT IT IS THE COMPLETE AND EXCLUSIVE STATEMENT OF THE AGREEMENT BETWEEN YOU AND ALTERA, WHICH SUPERSEDES ANY PROPOSAL OR PRIOR AGREEMENT, ORAL OR WRITTEN, AND ANY OTHER COMMUNICATIONS BETWEEN YOU AND ALTERA RELATING TO THE SUBJECT MATTER OF THIS AGREEMENT.

Index

Section I: 	Power

Section II: 	Configuration

Section III: 	I/O

a:	Clock Pins

b:	Dedicated and Dual Purpose Pins

c: 	Dual Purpose Differential I/O pins

Section IV: 	External Memory Interface Pins

a:	DDR/2 Interface pins

b:	DDR/2 Termination Guidelines

c:	QDRII/+ Interface pins

d:	QDRII/+ Termination Guidelines

e:	RLDRAMII Interface pins

f:	RLDRAMII Termination Guidelines

Section V:	Document Revision History

Section I: Power (AE Name)

Stratix II Recommended Reference Literature/Tool List

Stratix II Pin Out Files

Stratix II GX Device Family  Pin Connection Guidelines (PDF)

Power Supply Integrity Support Page (General decoupling guidelines)

Power Delivery Network (PDN) Tool

Power Delivery Network (PDN) Tool User Guide (PDF)

Early Power Estimator

PowerPlay Early Power Estimator User Guide for Stratix II, Stratix II GX, and HardCopy II (PDF)

PowerPlay Power Analyzer Support Resources

Altera Board Design Resource Center (General board design guidelines, PDN design, isolation, tools, and more)

AN 597: Getting Started Flow for Board Designs (PDF)

Stratix II FPGA Family Errata Sheet (PDF)

Index

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCINT |  | All VCCINT pins require a 1.2V supply. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |
| VCCIO[1..8] |  | Supported voltages are 1.5V, 1.8V, 2.5V, 3.3V. 1.2V is supported on VCCIO[4,7,8] for 1.2V HSTL I/O standards. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCPD[1..8] |  | The VCCPD pins require 3.3V and must ramp-up from 0V to 3.3V within 100ms to ensure successful configuration. For Secure Configuration this needs to power to 3.7V for no longer than one minute (on VCCPD[8] only). TDO buffer is powered by VCCIO not VCCPD. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been meet or list required actions for compliance. See Notes (1-1) (1-2). |
| GND |  | All GND pins should be connected to the board GND plane. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |
| VREFB[1..8]N[4..0] (not all pins are available in each device / package combination) |  | Input reference voltage for each I/O bank. VREF pins for each I/O bank are internally shorted together and must be connected to the same voltage level. If VREF pins are not used, designers should connect them to either the VCCIO in the bank in which the pin resides or GND. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCC_PLL5_OUT |  | This pin should be connected to the voltage level of the target device which PLL5 in bank 9 is driving. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |
| VCC_PLL6_OUT |  | This pin should be connected to the voltage level of the target device which PLL6 in bank 10 is driving. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCC_PLL11_OUT (not all pins are available in each device / package combination) |  | This pin should be connected to the voltage level of the target device which PLL11 in bank 11 is driving. For devices which do not have PLL11, but do have bank 11, VCCIO for bank 3 powers the I/O pins for bank 11. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |
| VCC_PLL12_OUT (not all pins are available in each device / package combination) |  | This pin should be connected to the voltage level of the target device which PLL12 in bank 12 is driving. For devices which do not have PLL12, but do have bank 12, VCCIO for bank 8 powers the I/O pins for bank 12. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCA_PLL[1..12] (not all pins are available in each device / package combination) |  | The designer is required to connect these pins to 1.2V, even if the PLL is not used. Use an isolated linear supply. Power on the PLLs operating at the same frequency should be decoupled. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |
| VCCD_PLL[1..12] (not all pins are available in each device / package combination) |  | The designer is required to connect these pins to 1.2V, even if the PLL is not used. Power on the PLLs operating at the same frequency should be decoupled. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |
| GNDA_PLL[1..12] (not all pins are available in each device / package combination) |  | All GNDA_PLL pins should be connected to the board GND plane. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |

Index  Top of Section

Notes:

1-1. This worksheet does not calculate required decoupling, it is expected the designer will select decoupling based on analysis of power required and impedance of power path required based on static and switching current values.  Refer to Altera’s Power Supply Integrity Web Support Page and Power Delivery Network (PDN) Tool for further information.

Capacitance values for the power supply should be selected after consideration of the amount of power they need to supply over the frequency of operation of the particular circuit being decoupled. A target impedance for the power plane should be calculated based on current draw and voltage drop requirements of the device/supply. The power plane should then be decoupled using the appropriate number of capacitors. On-board capacitors do not decouple higher than 100 MHz due to “Equivalent Series Inductance” of the mounting of the packages. Proper board design techniques such as interplane capacitance with low inductance should be considered for higher frequency decoupling.

Altera highly recommends using an independent PCB via for each independent power or ground ball on the package.  Sharing power or ground pin vias on the PCB could lead to noise coupling into the device and result in reduced jitter performance.

1-2. This worksheet does not include power estimation for the different power supplies provided.  Ensure each power supply is adequate for the device current requirements.  Refer to Altera’s Early Power Estimator Tools and PowerPlay Power Analyzer Support Resources for further guidance.

Use Altera’s Early Power Estimator Tools to ensure the junction temperature of the device is within operating specifications based on your design activity.

Additional Comments:

Index  Top of Section

Section II: Configuration (AE Name)

Configuration & Remote System Upgrades (PDF)

Stratix II GX Device Family  Pin Connection Guidelines (PDF)

Configuring Stratix II & Stratix II GX Devices (PDF)

USB-Blaster Download Cable User Guide (PDF)

ByteBlaster II Download Cable User Guide (PDF)

AN 597: Getting Started Flow for Board Designs (PDF)

Stratix II FPGA Family Errata Sheet (PDF)

Index

| Configuration Scheme | Configuration Voltage | VCCIO of Configuration banks |
| --- | --- | --- |

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| nIO_PULLUP |  | Dedicated input that chooses whether the internal pull-up resistors on the user I/O pins and dual-purpose I/O pins (nCSO, nASDO, DATA[7..0], nWS, nRS, RDYnBSY, nCS, CS, RUnLU, PGM[], CLKUSR, INIT_DONE, DEV_OE, DEV_CLR) are on or off before and during configuration. A logic high (1.5V, 1.8V, 2.5V, 3.3V) turns off the weak internal pull-up resistors, while a logic low turns them on. The nIO-PULLUP can be tied directly to VCCPD, use a 1-kΩ pull-up resistor, or tied directly to GND, depending on how the device is used. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCSEL |  | Dedicated input that selects which input buffer is used on configuration input pins: nCONFIG, DCLK (when used as an input), DATA[7..0], RUnLU, nCE, nWS, nRS, CS, nCS, and CLKUSR. The 3.3V/2.5V input buffer is powered by VCCPD, while the 1.8V/1.5V input buffer is powered by VCCIO. A logic high (VCCPD) selects the 1.8V/1.5V input buffer, while a logic low selects the 3.3V/2.5V input buffer. VCCSEL should be set to comply with the logic levels driven out of the configuration device or MAX II device/microprocessor with flash memory. The VCCSEL input buffer is powered by VCCPD and must be hardwired to VCCPD in order to enable the 1.8V/1.5V input buffers for configuration. VCCSEL tied to GND will enable a 3.3V/2.5V POR trip point, which may be above 1.8V. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DCLK |  | Dedicated configuration clock pin. In PS and FPP configuration, DCLK is used to clock configuration data from an external source into the Stratix II device. In AS mode, DCLK is an output from the Stratix II device that provides timing for the configuration interface. In PPA mode, DCLK should be tied to VCC to prevent this pin from floating. | Verify Guidelines have been met or list required actions for compliance. |
| MSEL[3..0] |  | Do not leave these pins floating. When these pins are unused, connect them to GND. Depending on the configuration scheme used, these pins should be tied to VCCPD or GND either directly or through 0-Ω resistors. Refer to Configuring Stratix II and Stratix II GX Devices (PDF) If only JTAG configuration is used, connect these pins to ground. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| nCE |  | In multi-device configuration, nCE of the first device is tied low while its nCEO pin drives the nCE of the next device in the chain. In single device configuration and JTAG programming, nCE should be connected directly to GND or through a 10k-Ω pull-down to GND if using an Active Serial header. | Verify Guidelines have been met or list required actions for compliance. |
| nCONFIG |  | Dedicated configuration control input. Pulling this pin low during user mode will cause the FPGA to lose its configuration data, enter a reset state, and tri-state all I/O pins. Returning this pin to a logic high level will initiate reconfiguration. nCONFIG should be connected directly to the configuration controller when the FPGA uses a passive configuration scheme, or through a 10-kΩ resistor to VCCPD when using Active Serial configuration scheme. | Verify Guidelines have been met or list required actions for compliance. |
| CONF_DONE |  | Pull high to VCCIO via an external 10-kΩ resistor, unless internal pull-up resistors on the enhanced configuration device are used. When using EPC2 devices, external 10-kΩ pull-up resistors must be used. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| nCEO |  | During multi-device configuration, this pin feeds the nCE pin of a subsequent device. During single-device configuration, this pin is left floating. For Connection Guidelines on how to connect nCEO in a chain with multiple voltages across the devices in the chain, refer to Stratix II Architecture (PDF). | Verify Guidelines have been met or list required actions for compliance. |
| nSTATUS |  | Pull high to VCCIO via a 10-kΩ resistor, unless internal pull-up resistors on the enhanced configuration device are used. When using EPC2 devices, external 10-kΩ pull-up resistors must be used. | Verify Guidelines have been met or list required actions for compliance. |
| PORSEL |  | The PORSEL pin should be tied directly to VCCPD or GND. | Verify Guidelines have been met or list required actions for compliance. |
| Optional/Dual-Purpose Configuration Pins |  |  |  |
| nCSO |  | When not programming the device in AS mode, nCSO is not used. Also, when this pin is not used as an I/O, Altera recommends that you leave the pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| ASDO |  | When not programming the device in AS mode, ASDO is not used. Also, when this pin is not used as an I/O, Altera recommends that you leave the pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| CRC_ERROR |  | When the dedicated output for CRC_ERROR is not used and this pin is not used as an I/O, Altera recommends that you leave the pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| DEV_CLRn |  | This pin is optional and allows you to override all clears on all device registers. When the dedicated input DEV_CLR is not used and this pin is not used as an I/O, Altera recommends that you tie this pin to VCCPD or ground. | Verify Guidelines have been met or list required actions for compliance. |
| DEV_OE |  | This pin is optional and allows you to override all tri-states on the device. When the dedicated input DEV_OE is not used and this pin is not used as an I/O, Altera recommends that you tie this pin to VCCPD or ground. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DATA0 |  | Dual-purpose configuration data input pin. The DATA0 pin can be used for bit-wide configuration or as an I/O pin after configuration is complete. When the dedicated input for DATA0 is not used and it is not used as an I/O, Altera recommends that you leave this pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| DATA[6..1] |  | When the dedicated inputs for DATA[6..1] are not used and these pins are not used as an I/O, Altera recommends that you leave these pins unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| DATA7 |  | When the dedicated input for DATA7 is not used and it is not used as an I/O, Altera recommends that you leave this pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| INIT_DONE |  | Connect this pin to a 10-kΩ resistor to VCCIO3. | Verify Guidelines have been met or list required actions for compliance. |
| nCS, CS |  | When the dedicated inputs for nCS, CS are not used and these pins are not used as an I/O, Altera recommends that you leave these pins unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| nRS |  | If the nRS pin is not used in PPA mode, it should be tied to VCCIO8. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| nWS |  | If the device is not being programmed in PPA mode and the pin is not being used, Altera recommends that you connect the nWS pin to the power bank this pin resides in. | Verify Guidelines have been met or list required actions for compliance. |
| CLKUSR |  | If the CLKUSR pin is not used as a configuration clock input and the pin is not used as an I/O, Altera recommends that you connect this pin to ground. | Verify Guidelines have been met or list required actions for compliance. |
| RDYnBSY |  | If the device is not being programmed in PPA mode and the pin is not being used as an I/O, Altera recommends that you leave the RDYnBSY pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| PGM[2..0] |  | If the PGM[2..0] pins are not used as page select output and these pins are not used as I/O, Altera recommends that you leave these pins unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| RUnLU |  | If the RUnLU pin is not used as a local or remote configuration input and the pin is not used as an I/O, Altera recommends that you leave this pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| TCK |  | Connect this pin to a 1-kΩ pull-down resistor to GND. The JTAG circuitry can be disabled by connecting TCK to GND. Treat this signal like a clock and follow typical clock routing guidelines. | Verify Guidelines have been met or list required actions for compliance. |
| TMS |  | Connect this pin through a pull up resistor with a value between 1-kΩ and 10-kΩ to VCCPD. The JTAG circuitry can be disabled by connecting TMS to VCC. | Verify Guidelines have been met or list required actions for compliance. See Note (2-1). |
| TDI |  | Connect this pin through a pull up resistor with a value between 1-kΩ and 10-kΩ to VCCPD. The JTAG circuitry can be disabled by connecting TDI to VCC. | Verify Guidelines have been met or list required actions for compliance. See Note (2-1). |
| TDO |  | Connect TDO to the correct JTAG interface signal. To disable JTAG circuitry, leave TDO unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| TRST |  | Connect TRST directly to VCCPD if JTAG circuitry is used. To disable JTAG circuitry, connect TRST to GND. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| JTAG Header |  | Power the ByteBlaster II or USB-Blaster cable’s VCC (pin 4 of the header) with the same supply as the VCCIO of the I/O bank that contains the JTAG pins. For multi-device JTAG chains with different VCCIO voltages, voltage translators may be required to meet the I/O voltages for the devices in the chain and JTAG header. The ByteBlaster II and USB-Blaster cables do not support a target supply voltage of 1.2 V. For the target supply voltage value, refer to the ByteBlaster II Download Cable User Guide and the USB-Blaster Download Cable User Guide. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

2-1. The pull-up resistor should be connected to the same supply voltage as the USB Blaster, MasterBlaster (VIO pin), ByteBlaster II, or ByteBlasterMV cable.

Additional Comments:

Index  Top of Section

Section III: I/O (AE Name)

Stratix II Recommended Reference Literature/Tool List

Stratix II Pin Out Files

Stratix II GX Device Family  Pin Connection Guidelines (PDF)

Stratix II Signal Integrity Center

Altera Board Design Resource Center (General board design guidelines, PDN design, isolation, tools, and more)

AN 597: Getting Started Flow for Board Designs (PDF)

Index

| Part A: Clock Pins |
| --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| CLK[1,3,9,11]p |  | These pins can be used as single ended or differential clock input pins or general single ended or differential input pins. Connect unused pins to the bank VCCIO or GND. Use dedicated clock pins to drive clocks into the device. These pins can connect to the device PLLs. These pins do not support differential OCT. These pins can only be used as inputs, they do not support output functions. These pins do not support the programmable weak internal pull up resistor option. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |
| CLK[1,3,9,11]n |  | These pins can be used as general single ended input pins or negative clock input pins for differential clock input. Connect unused pins to GND. When used as single ended inputs, these pins do not connect to the global / regional networks and cannot drive PLL inputs. These pins can only be used as inputs, they do not support output functions. These pins do not support the programmable weak internal pull up resistor option. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| CLK[0,2,8,10]p /DIFFIO_RX_C[0..1]p |  | These pins can be used as single ended I/O pins, single ended clock input pins with PLL connectivity, the positive terminal data pins of differential receiver channels, or the positive terminal of differential clocks. These pins support differential OCT. Unused pins can be tied to GND or unconnected. If unconnected, use Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |
| CLK[0,2,8,10]n/ DIFFIO_RX_C[0..1]n |  | These pins can be used as I/O pins, the negative clock input pins for differential clock input, or the negative data pins of differential receiver channels. When used as single ended inputs, these pins do not connect to the global / regional networks and cannot drive PLL inputs. Unused pins can be tied to GND or unconnected. If unconnected, use Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| CLK[4-7,12-15]p |  | These pins can be used as single ended or positive differential clock input pins with PLL connectivity or general single ended or positive differential input pins. They can also be used as general single ended output pins. These pins do not support differential OCT. These pins can be used for input or output (non-differential) operations. Unused pins can be tied to GND or unconnected. If unconnected, use Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |
| CLK[4-7,12-15]n |  | These pins can be used as single ended or negative differential clock input pins with PLL connectivity or general single ended or negative differential input pins. They can also be used as general single ended output pins. These pins can connect to the global / regional networks. Unused pins can be tied to GND or unconnected. If unconnected, use Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| FPLL[7..10]CLKp (not all pins are available in each device / package combination) |  | Dedicated positive clock inputs for fast PLLs (PLLs 7 through 10) which can also be used for data inputs. Connect unused pins to the bank VCCIO or GND. These pins do not support differential OCT. These pins do not connect to the global / regional networks. These pins can only be used as inputs, they do not support output functions. These pins do not support the programmable weak internal pull up resistor option. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |
| FPLL[7..10]CLKn (not all pins are available in each device / package combination) |  | Dedicated negative clock inputs for fast PLLs (PLLs 7 through 10) which can also be used for data inputs. Connect unused pins to GND. When used as single ended input, this pin does not connect to a PLL. These pins do not connect to the global / regional networks, and they cannot be used for output functions. These pins do not support the programmable weak internal pull up resistor option. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| PLL5_OUT[1,0]p |  | Optional positive external clock outputs [1,0] from enhanced PLL 5. These pins can be differential (two output pin pairs) or single ended (four clock outputs from PLL5). These pins cannot be used as differential inputs, but can be used as general purpose I/O pins if not used as PLL outputs. These pins support LVDS and LVPECL output operations when VCC_PLL5_OUT is powered by 3.3V. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |
| PLL5_OUT[1,0]n |  | Optional negative external clock outputs [1,0] from enhanced PLL 5. These pins can be differential (two output pin pairs) or single ended (four clock outputs from PLL5). These pins cannot be used as differential inputs, but can be used as general purpose I/O pins if not used as PLL outputs. These pins support LVDS and LVPECL output operations when VCC_PLL5_OUT is powered by 3.3V. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| PLL6_OUT[1,0]p |  | Optional positive external clock outputs [1,0] from enhanced PLL 6. These pins can be differential (two output pin pairs) or single ended (four clock outputs from PLL6). These pins cannot be used as differential inputs, but can be used as general purpose I/O pins if not used as PLL outputs. These pins support LVDS and LVPECL output operations when VCC_PLL6_OUT is powered by 3.3V. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |
| PLL6_OUT[1,0]n |  | Optional negative external clock outputs [1,0] from enhanced PLL 6. These pins can be differential (two output pin pairs) or single ended (four clock outputs from PLL6). These pins cannot be used as differential inputs, but can be used as general purpose I/O pins if not used as PLL outputs. These pins support LVDS and LVPECL output operations when VCC_PLL6_OUT is powered by 3.3V. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| PLL11_OUT[1,0]p (not all pins are available in each device / package combination) |  | Optional positive external clock outputs [1,0] from enhanced PLL 11. These pins can be differential (two output pin pairs) or single ended (four clock outputs from PLL11). These pins cannot be used as differential inputs, but can be used as general purpose I/O pins if not used as PLL outputs. These pins support LVDS and LVPECL output operations when VCC_PLL11_OUT is powered by 3.3V. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |
| PLL11_OUT[1,0]n (not all pins are available in each device / package combination) |  | Optional negative external clock outputs [1,0] from enhanced PLL 11. These pins can be differential (two output pin pairs) or single ended (four clock outputs from PLL11). These pins cannot be used as differential inputs, but can be used as general purpose I/O pins if not used as PLL outputs. These pins support LVDS and LVPECL output operations when VCC_PLL11_OUT is powered by 3.3V. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| PLL12_OUT[1,0]p (not all pins are available in each device / package combination) |  | Optional positive external clock outputs [1,0] from enhanced PLL 12. These pins can be differential (two output pin pairs) or single ended (four clock outputs from PLL12). These pins cannot be used as differential inputs, but can be used as general purpose I/O pins if not used as PLL outputs. These pins support LVDS and LVPECL output operations when VCC_PLL12_OUT is powered by 3.3V. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |
| PLL12_OUT[1,0]n (not all pins are available in each device / package combination) |  | Optional negative external clock outputs [1,0] from enhanced PLL 12. These pins can be differential (two output pin pairs) or single ended (four clock outputs from PLL12). These pins cannot be used as differential inputs, but can be used as general purpose I/O pins if not used as PLL outputs. These pins support LVDS and LVPECL output operations when VCC_PLL12_OUT is powered by 3.3V. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| PLL[5..6]_FBp/OUT2p |  | These pins can be used as I/O pins, positive external feedback input pins or external clock outputs for PLL[5,6]. These pins can be configured as general I/O, as positive differential input, or as positive differential output. They do not support bidirectional differential operations, and do not support differential OCT. Differential standards are supported when VCC_PLL[5..6]_OUT is powered by 3.3V. Unused pins can be connected to GND, or internally biased with Quartus II software reserve pin settings. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |
| PLL[5..6]_FBn/OUT2n |  | These pins can be used as I/O pins, negative external feedback input pins or external clock outputs for PLL[5,6]. These pins can be configured as general I/O, as negative differential input, or as negative differential output. They do not support bidirectional differential operations, and do not support differential OCT. Differential standards are supported when VCC_PLL[5..6]_OUT is powered by 3.3V. Unused pins can be connected to GND, or internally biased with Quartus II software reserve pin settings. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| PLL[11..12]_FBp/OUT2p (not all pins are available in each device / package combination) |  | These pins can be used as I/O pins, positive external feedback input pins or external clock outputs for PLL[11,12]. These pins can be configured as general I/O, as positive differential input, or as positive differential output. They do not support bidirectional differential operations, and do not support differential OCT. Differential standards are supported when VCC_PLL[11..12]_OUT is powered by 3.3V. Unused pins can be connected to GND, or internally biased with Quartus II software reserve pin settings. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |
| PLL[11..12]_FBn/OUT2n (not all pins are available in each device / package combination) |  | These pins can be used as I/O pins, negative external feedback input pins or external clock outputs for PLL[11,12]. These pins can be configured as general I/O, as negative differential input, or as negative differential output. They do not support bidirectional differential operations, and do not support differential OCT. Differential standards are supported when VCC_PLL[11..12]_OUT is powered by 3.3V. Unused pins can be connected to GND, or internally biased with Quartus II software reserve pin settings. | Verify Guidelines have been met or list required actions for compliance. See Note (3-1). |

Index  Top of Section

Notes:

3-1.  Refer to Knowledge Database solution rd12102002_3281 for further information regarding the concerns when I/O pins are left floating with no internal or external bias.  Ensure there are no conflicts between the Quartus II software device wide default configuration for unused I/Os and the board level connection.  Altera recommends setting unused I/O pins on a project wide basis to behave as inputs tri-state with weak pull up resistor enabled.  Individual unused pins can be reserved with specific behavior such as output driving ground or as output driving VCC to comply with the PCB level connection.

Additional Comments:

Index  Top of Section

| Part B: Dedicated and Dual Purpose Pins |
| --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| NC |  | Do not drive signals into these pins. When migrating devices, in some cases NC pins need to be connected to VCC/GND to allow successful migration see Knowledge Database solution rd03132006_933. | Verify Guidelines have been met or list required actions for compliance. |
| RUP4 |  | Reference pin for using calibrated OCT. Connect the RUP pin via a 25-Ω or 50-Ω precision resistor to the bank VCCIO supply. If this pin is not used for calibrated OCT, or not used as an I/O pin, it is recommended that the pin be connected to VCCIO4 or GND. If I/O banks 3 and 4 have different VCCIO levels, then only bank 4 can use calibrated OCT. | Verify Guidelines have been met or list required actions for compliance. See Note (3-2). |
| RDN4 |  | Reference pin for using calibrated OCT. Connect the RDN pin via a 25-Ω or 50-Ω precision resistor to GND. If this pin is not used for calibrated OCT, or not used as an I/O pin, it is recommended that the pin be connected to GND. If I/O banks 3 and 4 have different VCCIO levels, then only bank 4 can use calibrated OCT. | Verify Guidelines have been met or list required actions for compliance. See Note (3-2). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| RUP7 |  | Reference pin for using calibrated OCT. Connect the RUP pin via a 25-Ω or 50-Ω precision resistor to the bank VCCIO supply. If this pin is not used for calibrated OCT, or not used as an I/O pin, it is recommended that the pin be connected to VCCIO7 or GND. If I/O banks 7 and 8 have different VCCIO levels, then only bank 7 can use calibrated OCT. | Verify Guidelines have been met or list required actions for compliance. See Note (3-2). |
| RDN7 |  | Reference pin for using calibrated OCT. Connect the RDN pin via a 25-Ω or 50-Ω precision resistor to GND. If this pin is not used for calibrated OCT, or not used as an I/O pin, it is recommended that the pin be connected to GND. If I/O banks 7 and 8 have different VCCIO levels, then only bank 7 can use calibrated OCT. | Verify Guidelines have been met or list required actions for compliance. See Note (3-2). |
| PLL_ENA |  | If a PLL uses the pllena port, drive the PLL_ENA pin low to reset all PLLs, including the counters, to their default state. If VCCSEL = 0, then you must drive the PLL_ENA with a 3.3/2.5V signal to enable the PLLs. If VCCSEL = 1, connect PLL_ENA to 1.8/1.5V to enable the PLLs. If no PLLs use the pllena port, this pin can be tied to GND. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| TEMPDIODEp,n |  | If the temperature sensing diode is not used, connect these pins to GND. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

3-2. Refer to Knowledge Database solution rd12102002_3281 for further information regarding the concerns when I/O pins are left floating with no internal or external bias.  Ensure there are no conflicts between the Quartus II software device wide default configuration for unused I/Os and the board level connection.  Altera recommends setting unused I/O pins on a project wide basis to behave as inputs tri-state with weak pull up resistor enabled.  Individual unused pins can be reserved with specific behavior such as output driving ground or as output driving VCC to comply with the PCB level connection.

Additional Comments:

Index  Top of Section

| Part C: Dual Purpose Differential I/O pins |
| --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| DIFFIO_RX[]p,n (Refer to the device Pin Table for number of channels based on device selected) |  | Dual-purpose differential receiver channels. These channels can be used for receiving LVDS-compatible signals. Pins with a "p" suffix carry the positive signal for the differential channel. Pins with an "n" suffix carry the negative signal for the differential channel. These pins support OCT Rd. These pins do not support differential transmitter operations. If not used for differential signaling, these pins are available as single ended user I/O pins. Unused pins can be tied to GND or unconnected. If unconnected, use Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (3-3). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DIFFIO_TX[]p,n (Refer to the device Pin Table for number of channels based on device selected) |  | Dual-purpose differential transmitter channels. These channels can be used for transmitting LVDS-compatible signals. Pins with a "p" suffix carry the positive signal for the differential channel. Pins with an "n" suffix carry the negative signal for the differential channel. These pins do not support differential receiving operations. If not used for differential signaling, these pins are available as single ended user I/O pins. Unused pins can be tied to GND or unconnected. If unconnected, use Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (3-3). |

Notes:

3-3.  Unused I/O pins can be configured as outputs driving ground, or as inputs tristate with the weak pull up resistor enabled to prevent them from floating.  Refer to Knowledge Database solution rd12102002_3281 for further information regarding the concerns when I/O pins are left floating with no internal or external bias.  Ensure there are no conflicts between the Quartus II software device wide default configuration for unused I/Os and the board level connection.  Altera recommends setting unused I/O pins on a project wide basis to behave as inputs tri-state with weak pull up resistor enabled.  Individual unused pins can be reserved with specific behavior such as output driving ground or as output driving VCC to comply with the PCB level connection.

Index  Top of Section

Additional Comments:

Index  Top of Section

Section IV: External Memory Interface Pins (AE Name)

Stratix II  Literature

External Memory Interfaces in Stratix II & Stratix II GX Devices (PDF)

Stratix II Pin Out Files

Stratix II GX Device Family  Pin Connection Guidelines (PDF)

Altera Board Design Resource Center (General board design guidelines, PDN design, isolation, tools, and more)

External Memory Interface Literature

AN 449: External Memory Interface Design Guidelines for Stratix II, Stratix II GX, and Arria GX Devices (PDF)

Board Layout Guidelines (PDF)

DDR and DDR2 Literature

AN 328: Interfacing DDR2 SDRAM with Stratix II, Stratix II GX, and Arria GX Devices (PDF)

Board Layout Guidelines (PDF)

QDRII/+ Literature

AN 326: Interfacing QDRII+ & QDRII with Stratix II, Stratix II GX, Stratix, & Stratix GX Devices (PDF)

RLDRAMII Literature

AN 325: Interfacing RLDRAM II with Stratix II, Stratix & Stratix GX Devices (PDF)

Index

| Part A: DDR/2 Interface Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Data pins - DQ |  | Place it on DQ pins of the DQ/DQS group. The order of the DQ bits within a designated DQ group/bus is not important; however, use caution when making pin assignments if you plan on migrating to a different memory interface that has a different DQ bus width (e.g. migrating from x4 to x8). Analyze the available DQ pins across all pertinent DQS columns in the pin list. | Verify Guidelines have been met or list required actions for compliance. |
| Data strobe - DQS/DQSn |  | Only Single ended DQS is supported. Connect the DQS pin to the DQS pin of the corresponding DQ/DQS group. | Verify Guidelines have been met or list required actions for compliance. |
| Data Mask DM |  | Place it on one of the DQ pins in the group. DM pins need to be part of the write DQS/DQ group. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| mem_clk and mem_clk_n |  | PLL dedicated clock output pin pairs on the same side as the interface resides. DQS/DQSn pin pair in the same bank or side as the interface resides. If the above pins are not available, memory clock can be assigned any regular I/O pins. Dedicated PLL clock output pins are ideal for memory clock pins as they are optimized for SI, but if the design is big and the data pins are using up all top bank pins then LVDS pin pairs on the side banks of the device can be used. | Verify Guidelines have been met or list required actions for compliance. |
| clock_source |  | The clock input pin of the system PLL should be on the same side or same bank of the device as the data, address and command signals. (CLK[4..7]&[12..15]p/n pair can be used as input clock pin. For single ended clock sources, ALWAYS use the p pin of the dedicated clock inputs. | Verify Guidelines have been met or list required actions for compliance. |
| Address |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● mem_clk* pins. ● DQ, DQS, or DM pins. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Command |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● mem_clk* pins. ● DQ, DQS, or DM pins. | Verify Guidelines have been met or list required actions for compliance. |
| Reset |  | Dedicated clock input pin. (high fan-out signal) | Verify Guidelines have been met or list required actions for compliance. |
| Fedback_clk_in (only for legacy controller) |  | Fedback_clk_in signal can be assigned to dedicated PLL clock pins that go directly to PLL input pin. (CLK[4..7] & [12..15]p can be used for this. | Verify Guidelines have been met or list required actions for compliance. |
| Fedback_clk_out (only for legacy controller) |  | Fedback_clk_out signal can be assigned to any user I/O pin in the same bank as the rest of the signals. | Verify Guidelines have been met or list required actions for compliance. |
| RUP[4,7], RDN[4,7] |  | Used when calibrated OCT for the memory interface pins is implemented. RUP & RDN should be in a 1.8V VCCIO bank. Make sure that the VCCIO of your DDR2 interface bank and the VCCIO of the bank with RUP, RDN pin match. If the RUP and RDN pins are used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Part B: DDR/2 Termination Guidelines |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Memory clocks @ Memory |  | Memory clocks use Unidirectional class I termination. They are typically differentially terminated with an effective 100-Ω resistance. For DIMM no termination is required as termination is placed on the DIMM itself. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Memory clocks @ FPGA |  | Use series 50-Ω output termination without calibration on the FPGA side by sourcing <variation_name>_pin_assignments.tcl file to make these assignments automatically for hp ddr2 controller. For legacy ddr2 controller manually assign these assignments in the assignment editor. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| DQS@Memory |  | For DDR2 use ODT feature. For DDR use 50-Ω external parallel termination. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DQS @ FPGA |  | Use series 25-Ω without calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically for hp ddr2 controller. For legacy ddr2 controller manually assign these assignments in the assignment editor. Use parallel 50-Ω as input termination for both controllers. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| DQ @ Memory |  | For DDR2 use ODT feature. For DDR use 50-Ω external parallel termination. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| DQ @ FPGA |  | Use series 25-Ω without calibration as output termination. Source <variation_name>_pin_assignments.tcl file to assign these assignments automatically for hp ddr2 controller. For legacy ddr2 controller manually assign these assignments in the assignment editor. Use parallel 50-Ω as input termination for both controllers. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| DM@ Memory |  | For DDR2 use ODT. For DDR Use 50-Ω external parallel termination. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DM @ FPGA |  | Use series 50-Ω without calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. For legacy ddr2 controller manually assign these assignments in the assignment editor. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Address [BA, mem_addr] @ Memory |  | Unidirectional class I termination. For multi-loads Altera recommends the ideal topology is a balanced symmetrical tree. Altera recommends that the class I termination to VTT is placed: ■ At the DIMM connector (for interfaces using DIMMs). ■ At the first split or division of the symmetrical tree for discrete devices. Nonsymmetrical topologies or DIMMs result in over or undershoot and oscillations on the line, which may require compensation capacitors or a lower than ideal drive strength to be specified resulting in de-rated interface performance. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Address [BA, mem_addr] @ FPGA |  | Use maximum current strength setting. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically for hp ddr2 controller. For legacy ddr2 controller manually assign these assignments in the assignment editor. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Command [CKE, CS_N, RAS, CAS, WE_N] @ Memory |  | Unidirectional class I termination. All class I signals are multi-load signals—they either go to a DIMM that has multiple memory devices, or they go to all memory devices that make up the interface. Altera recommends the ideal topology is a balanced symmetrical tree. Altera recommends that the class I termination to VTT is placed: ■ At the DIMM connector (for interfaces using DIMMs) ■ At the first split or division of the symmetrical tree for discrete devices Nonsymmetrical topologies or DIMMs result in over or undershoot and oscillations on the line, which may require compensation capacitors or a lower than ideal drive strength to be specified resulting in derated interface performance. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Command [CKE, CS_N, RAS, CAS, WE_N] @ FPGA |  | Use maximum current strength setting. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically for hp ddr2 controller. For legacy ddr2 controller manually assign these assignments in the assignment editor. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Notes:

4-1. The termination schemes suggested in the table are general guidelines. You should do board level simulation for your particular system/board to determine optimal termination scheme.

Index  Top of Section

| Part C: Miscellaneous |  |  |  |
| --- | --- | --- | --- |
| Pin Description | Schematic Name | Connection Guidelines | Comments/ Issues |
| Vref |  | Use voltage regulator to generate this voltage | Verify Guidelines have been met or list required actions for compliance. See Note (4-2). |
| Vtt |  | Use voltage regulator to generate this voltage | Verify Guidelines have been met or list required actions for compliance. See Note (4-2). |
| RUP & RDN |  | RUP pin is connected to VCCIO (1.8V) through an external 50-Ω ±1% resistor . RDN pin is connected to GND through an 50-Ω ±1% resistor. If the RUP and RDN pins are used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

4-2. This worksheet does not calculate required decoupling, it is expected the designer will select decoupling based on analysis of power required and impedance of power path required based on static and switching current values.  Refer to Altera’s Power Supply Integrity Web Support Page and Power Delivery Network (PDN) Tool for further information.

Capacitance values for the power supply should be selected after consideration of the amount of power they need to supply over the frequency of operation of the particular circuit being decoupled. A target impedance for the power plane should be calculated based on current draw and voltage drop requirements of the device/supply. The power plane should then be decoupled using the appropriate number of capacitors. On-board capacitors do not decouple higher than 100 MHz due to “Equivalent Series Inductance” of the mounting of the packages. Proper board design techniques such as interplane capacitance with low inductance should be considered for higher frequency decoupling.

Additional Comments:

Index  Top of Section

| Part C: QDR II/+ Interface Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Q – Read data pins |  | The read side signals Q (In DQS Mode) are automatically placed by the auto_add_constraints.tcl script generated by the IP Tool Bench in the available DQ/DQS group. You can use any user I/O pins in the non-DQS mode. | Verify Guidelines have been met or list required actions for compliance. |
| D – Write data pins |  | It is ideal to have D pins and Q pins in the same bank. If the memory has wide interfaces and all the Q pins are assigned in one bank and there are no available pins for D pins, the D pins can be assigned to the adjacent same side bank. For maintaining tight skew between the D pins as Q pins and to meet fast interface timing, assign the D pins to the unassigned DQS (bus width) groups available within the bank. | Verify Guidelines have been met or list required actions for compliance. |
| Read clock to the FPGA - CQ/CQn |  | For DLL Based implementation: CQ – Place it on DQS pin CQn – Place it on DQSn pin of the corresponding group For PLL Based implementation: CQ – PLL dedicated clock input CQn – Not used | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Write clock from the FPGA - K/Kn |  | PLL dedicated clock output pin pairs DQS/DQSn pin pair in the same bank or side as the interface resides. Dedicated PLL clock output pins are ideal for memory clock pins as they are optimized for SI, but if the design is big and the data pins are using up all top bank pins then LVDS pin pairs on the side banks of the device can be used. Choosing dedicated PLL clock output pins also gives the user flexibility to either generate the memory clocks directly from the PLL or generate them from IOE elements later in the design cycle. You can also use user I/O pin for K and Kn if none of the above two options can be implemented. | Verify Guidelines have been met or list required actions for compliance. |
| Input clock for output data – C and Cn |  | Altera QDRII SRAM interface is implemented in single clock mode. Connect C and Cn high. Also, look for the connection guidance in the memory device datasheet. | Verify Guidelines have been met or list required actions for compliance. |
| QVLD |  | QVLD signal indicates that the read data coming to the FPGA is ready to be captured. Place it on the DQVLD pin in the corresponding DQ/DQS group. Only QDRII+ SRAM device has a QVLD pin. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| clock_source |  | Input clock pin to the QDRII/+ core PLL - Dedicated PLL clock input pin with direct (not using a global clock net) connection to the PLL and DLL required by the interface. | Verify Guidelines have been met or list required actions for compliance. |
| BWSn |  | Data Mask Pin – Place it on one of the DQ pins in the group. If not possible, you can also place this pin on any user I/O pin in the same bank. | Verify Guidelines have been met or list required actions for compliance. |
| Address |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● Clock pins. ● Data pins If the Q and D pins are assigned to one bank and if there are no available pin locations in the same bank then address signals should go to the adjacent same side bank. If you are using burst of 2 mode, staggering the address pins between two adjacent banks is recommended for SSN reasons. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Command |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● Clock pins. ● Data pins If the Q and D pins are assigned to one and if there are no available pin locations in the same bank then command signals should go to the adjacent same side bank. | Verify Guidelines have been met or list required actions for compliance. |
| Reset |  | Dedicated clock input pin. (high fan-out signal) | Verify Guidelines have been met or list required actions for compliance. |
| d_off |  | Refer to memory specification and guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| RUP[4,7] |  | Used when calibrated OCT for the memory interface pins is implemented. RUP pin should be connected to the VCCIO of the bank it is in and that bank should have the VCCIO of 1.5V or 1.8V. If the RUP pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |
| RDN[4,7] |  | Used when calibrated OCT for the memory interface pins is implemented. RDN pin should be connected to GND. If the RDN pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Part D: QDRII/+ Termination Guidelines |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Write Clock (K/Kn) @ FPGA |  | Class I termination scheme FPGA side termination can be implemented through OCT feature so that no board level termination required on the FPGA side. For the write clock signals Altera recommends series OCT 50-Ω with calibration. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Write Clock (K/Kn) @ Memory |  | Class I termination scheme Write clock at the memory side should be terminated with class I Parallel termination at the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Read Clock (CQ/CQn) @ FPGA |  | Class I termination scheme For the read clock signals Altera recommends using parallel OCT 50-Ω with calibration. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Read Clock (CQ/CQn) @ Memory |  | Read clock output impedance is implemented with the help of ZQ input pin on the memory device side. If not, you need to put 50-Ω series OCT on the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Write data - D @ FPGA |  | Use series 50-Ω with calibration as output termination. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Write data – D @ Memory |  | Write data at the memory side should be terminated with class I Parallel termination at the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Read data - Q @ FPGA |  | Use parallel 50-Ω with calibration as input termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Read data - Q @ Memory |  | Read data output impedance is implemented with the help of ZQ input pin on the memory device side. If not, you need to put 50-Ω series OCT on the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| BWSn @ FPGA |  | Use series 50-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| BWSn @ Memory |  | BWSn at the memory side should be terminated with class I Parallel termination at the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| QVLD @ FPGA |  | Use parallel 50-Ω with calibration as input termination. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Address @ FPGA |  | If there are multiple loads on certain FPGA output pins (for example, if the address bus is shared across many memory devices), use of maximum drive strength setting may be preferred over the series OCT setting. Use board level simulations to pick the optimal setting for best signal integrity. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Address @ Memory |  | On the memory side, Altera recommends the use of external parallel termination on input signals to the memory. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Command @ FPGA |  | If there are multiple loads on certain FPGA output pins (for example, if the address bus is shared across many memory devices), use of maximum drive strength setting may be preferred over the series OCT setting. Use board level simulations to pick the optimal setting for best signal integrity. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Command @ Memory |  | On the memory side, Altera recommends the use of external parallel termination on input signals to the memory. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Pin Description | Connection Guidelines | Comments/Issues |
| --- | --- | --- |
| Vref | Use a voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. See Note (4-2). |
| Vtt | Use a voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. See Note (4-2). |
| RUP & RDN | RUP pin is connected to VCCIO (1.5/1.8 V) through an external 50-Ω ±1% resistor . RDN pin is connected to GND through an 50-Ω ±1% resistor. If the RUP and RDN pins are used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. See Note (4-2). |

Index  Top of Section

| Part E: RLDRAM II Interface Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| DQ – Read and write pins for CIO |  | Assign it to the DQ pins of an available DQ/DQS pin group. The order of the DQ bits within a designated DQ group/bus is not important; however, use caution when making pin assignments if you plan on migrating to a different memory interface that has a different DQ bus width. Analyze the available DQ pins across all pertinent DQS columns in the pin list. | Verify Guidelines have been met or list required actions for compliance. |
| Q – Read data pins for SIO |  | For DLL based implementation: Assign it to the DQ pins of an available DQ/DQS pin group. The order of the DQ bits within a designated DQ group/bus is not important; however, use caution when making pin assignments if you plan on migrating to a different memory interface that has a different DQ bus width. Analyze the available DQ pins across all pertinent DQS columns in the pin list. For PLL based implementation: User I/O pin | Verify Guidelines have been met or list required actions for compliance. |
| D – Write data pins for SIO |  | It is ideal to have D pins and Q pins in the same bank. If the memory has wide interfaces and all the Q pins are assigned in one bank and there are no available pins for D pins, the D pins can be assigned to the adjacent same side bank. For maintaining tight skew between the D pins as Q pins and to meet fast interface timing, assign the D pins to the unassigned DQS (bus width) groups available within the bank. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Read clock to the FPGA - QK/QKn |  | For DLL based implementation: QK – Place it on DQS pin QKn – Not used For PLL based implementation: QK – Place it on dedicated PLL clock input QKn – Not used | Verify Guidelines have been met or list required actions for compliance. |
| Write clock from the FPGA - DK/DKn |  | DK – Place it on user I/O pin. DKn – Place it on user I/O pin. Use the same pin to drive CK and DK signals and another pin for CK# and DK# signals. You can use two different pins if Quartus II software reported skew between these pins meet the RLDRAM II device's tCKDK specification. | Verify Guidelines have been met or list required actions for compliance. |
| System clock for the RLDRAM II to sample address and command – CK/CKn |  | CK – Place it on user I/O pin. CKn – Place it on user I/O pin. Use the same pin to drive CK and DK signals and another pin for CK# and DK# signals. You can use two different pins if Quartus II software reported skew between these pins meet the RLDRAM II device's tCKDK specification. | Verify Guidelines have been met or list required actions for compliance. |
| Address |  | Any user I/O pin. To minimize skew, you should place address pins in the same bank or side of the device as the following pins: ● Clock pins. ● Data pins | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Command |  | Any user I/O pin. To minimize skew, you should place command pins in the same bank or side of the device as the following pins: ● Clock pins. ● Data pins | Verify Guidelines have been met or list required actions for compliance. |
| DM |  | Place it on the user I/O pin. | Verify Guidelines have been met or list required actions for compliance. |
| QVLD |  | QVLD signal indicates that the read data coming to the FPGA is ready to be captured. Place it in the QVLD pin of the read DQS/DQ group. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Part F: RLDRAMII Termination Guidelines |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Write Clock (DK/DKn) @ FPGA |  | Class I termination scheme FPGA side termination can be implemented through OCT feature so that no board level termination required on the FPGA side. For the write clock signals Altera recommends series OCT 50-Ω without calibration. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Write Clock (DK/DKn) @ Memory |  | Write clock at the memory side should be terminated with class I Parallel termination at the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Read Clock (QK/QKn) @ FPGA |  | For the read clock signals Altera recommends using parallel OCT 50-Ω with calibration. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Read Clock (QK/QKn) @ Memory |  | Read clock output impedance should be implemented by series OCT on the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Write data - D @ FPGA |  | For SIO Use series 50-Ω with calibration as output termination. For CIO Use Class II termination scheme with driver and received termination on both sides (FPGA and memory device) for read and write operations. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Write data – D @ Memory |  | For SIO Write data at the memory side should be terminated with class I Parallel termination at the memory side. For CIO Use Class II termination scheme with driver and received termination on both sides (FPGA and memory device) for read and write operations. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Read data - Q @ FPGA |  | For SIO Use parallel 50-Ω with calibration as input termination. For CIO Use Class II termination scheme with driver and received termination on both sides (FPGA and memory device) for read and write operations. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Read data - Q @ Memory |  | Use 50-Ω series termination at the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| BWSn @ FPGA |  | Use series 50-Ω with calibration as output termination. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| BWSn @ Memory |  | BWSn at the memory side should be terminated with class I Parallel termination at the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| QVLD @ FPGA |  | Use parallel 50-Ω with calibration as input termination. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| QVLD @ Memory |  | Use series 50-Ω as output termination. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Address @ FPGA |  | If there are multiple loads on certain FPGA output pins (for example, if the address bus is shared across many memory devices), use of maximum drive strength setting may be preferred over the series OCT setting. Use board level simulations to pick the optimal setting for best signal integrity. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Address @ Memory |  | On the memory side, Altera recommends the use of external parallel termination on input signals to the memory. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Command @ FPGA |  | If there are multiple loads on certain FPGA output pins (for example, if the address bus is shared across many memory devices), use of maximum drive strength setting may be preferred over the series OCT setting. Use board level simulations to pick the optimal setting for best signal integrity. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| Command @ Memory |  | On the memory side, Altera recommends the use of external parallel termination on input signals to the memory. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Pin Description | Connection Guidelines | Comments/Issues |
| --- | --- | --- |
| Vref | Use voltage regulator to generate this voltage | Verify Guidelines have been met or list required actions for compliance. See Note (4-2). |
| Vtt | Use voltage regulator to generate this voltage | Verify Guidelines have been met or list required actions for compliance. See Note (4-2). |
| RUP & RDN | RUP pin is connected to VCCIO (1.5/1.8 V) through an external 50-Ω ±1% resistor . RDN pin is connected to GND through an 50-Ω ±1% resistor. If the RUP and RDN pins are used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. See Note (4-2). |

Additional Comments:

Index  Top of Section

Section V: Document Revision History

| Revision | Changes Made | Date |
| --- | --- | --- |
| V2.1 | Updated pull up resistor values for TMS and TDI. Minor text and formatting edits throughout the document. | April 2010 |
| V2.0 | Initial Release, based on Stratix II GX Pin Connection Guidelines version 3.1. | May 2009 |

Index